## Slide 1: CSE 502: Computer Architecture
Instruction Commit

## Slide 2: The End of the Road (um… Pipe)
Commit is typically the last stage of the pipeline
Anything an insn. does at this point is irrevocable
  Only actions following sequential execution allowed
  E.g., wrong path instructions may not commit
    They do not exist in the sequential execution

## Slide 3: Everything Should Appear In-Order
ISA defines program execution in sequential order
To the outside, CPU must appear to execute in order
  When is someone looking?

## Slide 4: “Looking” at CPU State
When OS swaps contexts
  OS saves the current program state (requires “looking”)
  Allows restoring the state later
When program has a fault (e.g., page fault)
  OS steps in and “looks” at the “current” CPU state

## Slide 5: Implementation in the CPU
ARF keeps state corresponding to committed insns.
  Commit from ROB happens in order
  ARF always contains some RF state of sequential execution
Whoever wants to “look” should look in ARF
  What about insns. that executed out of order?

## Slide 6: Only the Sequential Part Matterns
LSQ
PRF
RS
fPC
ROB
PC
Memory
Sequential
View of the
Processor
PC
Memory
RF
State of the Superscalar
Out-of-Order Processor
RF
  What if there’s no ARF?

## Slide 7: View of the Unified Register File
PRF
sRAT
aRAT
If you need to “see” a register, you go through the aRAT first.
ARF

## Slide 8: View of Branch Mispredictions
ROB
LSQ
PRF
RS
fPC
PC
Memory
ARF
Mispredicted
Branch
Wrong-path instructions
are flushed…
architected state has
never been touched
Fetch correct path
instructions
Which can update the
architected state when
they commit
Notes: Most of the remaining slides should be review for anyone who’s taken a class on basic out-of-order processor organizations.

## Slide 9: Committing Instructions (1/2)
“Retire” vs. “Commit”
  Sometimes people use this to mean the same thing
  Sometimes they mean different things
    Check the context!
Insn. commits by making “effects” visible
  (A)RF, Memory/$, PC

## Slide 10: Committing Instructions (2/2)
When an insn. executes, it modifies processor state
  Update a register
  Update memory
  Update the PC
To make “effects” visible, core copies values
  Value from Physical Reg to Architected Reg
  Value from LSQ to memory/cache
  Value from ROB to Architected PC

## Slide 11: x86 Commit (1/2)
ROB contains uops, outside world knows insns.
ROB
uop 1 (ADD)
uop 1 (SUB)
commit
ADD EAX, EBX
SUB EBX, ECX
ADD EDX, [EAX]
commit
POPA
????
If we take an interrupt right now, we’ll see a half-executed instruction!
uop 1 (LD)
uop 2 (ADD)
uop 1 (POP)
uop 2 (POP)
uop 3 (POP)
uop 4 (POP)
uop 5 (POP)
uop 6 (POP)
uop 7 (POP)
uop 8 (POP)

## Slide 12: x86 Commit (2/2)
Works when uop-flow length ≤ commit width
What to do with long flows?
  In all cases: can’t commit until all uops in a flow completed
  Just commit N uops per cycle ... but make commit uninterruptable
ROB
uop 1
uop 2
uop 3
uop 4
uop 5
uop 6
uop 7
uop 8
commit
commit
POPA
Timer interrupt!
Defer: Can’t act on this yet...
Now do something about the interrupt.

## Slide 13: Handling REP-prefixed Instructions (1/2)
Ex. REP STOSB (memset EAX value ECX times)
  Entire sequence is one x86 instruction
  What if REPs for 1,000,000,000 iterations?
    Can’t “lock up” for a billion cycles while uops commit
    Can’t wait to commit until all uops are done
      Can’t even fetch the entire instruction – not enough space in ROB
At the ISA level, REP iterations are interruptible...
  Treat each iteration as a separate “macro-op”

## Slide 14: Handling REP-prefixed Instructions (2/2)
MOV EDI, <pointer> ; the array we want to memset
SUB EAX, EAX ; zero
CLD ; clear direction flag (REP fwd)
MOV ECX, 4 ; do for 100 iterations
REP STOSB ; memset!
ADD EBX, EDX ; unrelated instruction
MOV EDI, xxx
SUB EAX, EAX
CLD
MOV ECX, 4
uCMP ECX, 0
uJCZ
STA tmp, EDI
STD EAX, tmp
SUB ECX, 1
ADD EDI, 1
uCMP ECX, 0
uJCZ
STA tmp, EDI
STD EAX, tmp
SUB ECX, 1
ADD EDI, 1
uCMP ECX, 0
uJCZ
STA tmp, EDI
STD EAX, tmp
SUB ECX, 1
ADD EDI, 1
uCMP ECX, 0
uJCZ
STA tmp, EDI
STD EAX, tmp
SUB ECX, 1
ADD EDI, 1
uCMP ECX, 0
uJCZ
ADD EBX, EDX
Check for zero iterations
(could happen with MOV ECX, 0 )
MOVS flow
REP overhead for
1st iteration
MOVS flow
REP overhead
for 2nd iter.
MOVS flow
REP overhead
for 3rd iter
MOVS flow
REP
4th iter
A:
B:
C:
D:
All of these are interruptible points (commit can stop and effects be seen by outside world), since they all have well-defined ISA-level states:
A: ECX=3, EDI = ptr+1
B: ECX=2, EDI = ptr+2
C: ECX=1, EDI = ptr+3
D: ECX=0, EDI = ptr+4

## Slide 15: Blocked Commit
To commit N insns. per cycle, ROB needs N ports
  (in addition to ports for dispatch, issue, exec, and WB)
inst 1
inst 2
inst 3
inst 4
Four read ports
for four commits
ROB
inst 1
inst 2
inst 3
inst 4
One wide read port
ROB
Can’t reuse ROB entries until all in block have committed. Can’t commit across blocks.
  Reduces cost, lowers IPC due to constraints

## Slide 16: Faults
Divide-by-Zero, Overflow, Page-Fault
All occur at a specific point in execution (precise)
DBZ!
Trap
(resume execution)
Divide may have executed
before other instructions
due to OoO scheduling!
DBZ!
Trap?
(when?)
  CPU maintains appearance of sequential execution

## Slide 17: Timing of DBZ Fault
Need to hold on to your faults
RS
ROB
Exec:
DBZ
Architected
State
Let earlier instructions commit
The arch. state is the same
as just before the divide executed
in the sequential order
Now, raise the DBZ fault and
when you switch to the kernel,
everything appears as it should
On a fault, flush the
machine and switch
to the kernel
Just make note of the fault,
but don’t do anything (yet)

## Slide 18: Speculative Faults
Faults might not be faults…
ROB
DBZ!
Branch
Mispredict
The fault goes away
Which is what we want, since in a
sequential execution, the wrong-path divide
would not have executed (and faulted)
(flush wrong-path)
  Buffer faults until commit to avoid speculative faults

## Slide 19: Timing of TLB Miss
Store must re-execute (or re-commit)
  Cannot leave the ROB
TLB miss
Trap
(resume execution)
…
Walk page-table,
may find a page fault
Re-execute
store
  Store TLB miss can stall the core

## Slide 20: Load Faults are Similar
Load issues, misses in TLB
  When load is oldest, switch to kernel for page-table walk …could be painful; there are lots of loads
Modern processors use hardware page-table walkers
  OS loads a few registers with PT information (pointers)
  Simple logic fetches mapping info from memory
  Page-table format is specified by the ISA

## Slide 21: Asynchronous Interrupts
Some interrupts are not associated with insns.
  Timer interrupt
  I/O interrupt (disk, network, etc…)
  Low battery, UPS shutdown
When the CPU “notices” doesn’t matter (too much)
Key
Pressed
Key
Pressed
Key
Pressed

## Slide 22: Two Options for Handling Async Interrupts
Handle immediately
  Use current architected state and flush the pipeline
Deferred
  Stop fetching, let processor drain, then switch to handler
    What if CPU takes a fault in the mean time?
    Which came “first”, the async. interrupt or the fault?

## Slide 23: Store Retirement (1/2)
Stores forward to later loads (for same address)
  Normally, LSQ provides this facility
ld
17
st
ld
33
st
ld
D$
17
At commit, store
Updates cache
st
ld
After store has left
the LSQ, the D$
can provide the
correct value
D$
D$

## Slide 24: Store Retirement (2/2)
Can’t free LSQ Store entry until write is done
  Enables forwarding until loads can get value from cache
Have to re-check TLB when doing write
  TLB contents at Execute were speculative
Store may stall commit for a long time
  If there’s a cache miss
  If there’s a TLB miss (with HW TLB walk)
store
All instructions may have successfully
executed, but none can commit!

## Slide 25: Writeback Buffer (1/2)
Want to get stores out of the way quickly
store
D$
store
WB Buffer
ld
Even if store misses in
cache, entering WB buffer
counts as committing.
Allows other insns. to commit.
WB buffer is part of the cache
hierarchy. May need to provide
values to later loads.
Eventually, the cache
update occurs, the WB
buffer entry is emptied.
ld
Cache can now
provide the correct value.
  Usually fast, but potential structural hazard

## Slide 26: Writeback Buffer (2/2)
Stores enter WB Buffer in program order
Multiple stores can exist to same address
  Only the last store is “visible”
1234
42
Addr
Value
-1
13
90901
8
oldest
youngest
next to write
to cache
Load
42
5678
42
Store
42
Load
42
No one can “see” this store anymore!

## Slide 27: Write Combining Buffer (1/2)
Augment WBB to combine writes together
1234
42
Addr
Value
Load
42
5678
42
Store
42
Load
42
Only one writeback
Now instead of two
  If Stores to same address, combine the writes

## Slide 28: Write Combining Buffer (2/2)
Can combine stores to same cache line
1234
80
$-Line
Addr
Cache Line Data
Store
84
One cache write
can serve multiple
original store
instructions
Benefit: reduces cache
traffic, reduces pressure
on store buffers
5678
Aggressiveness of write-combining may be limited by memory ordering model
Writeback/combining buffer can be implemented in/integrated with the MSHRs
Only certain memory regions may be “write-combinable” (e.g., USWC in x86)

## Slide 29: Senior Store Queue
Use STQ as WBB (not necessarily write combining)
STQ
Store
Store
Store
Store
Store
Store
STQ head
STQ tail
DL1
L2
STQ head
STQ head
Store
Store
Store
Store
STQ tail
New stores cannot allocate into Senior STQ entries until stores complete
  No WBB and no stall on Store commit
While stores are completing, other accesses (loads, etc…) can continue getting the values from the “senior” STQ

## Slide 30: Retire
Insn. retires by cleaning up all related state
Besides updating architected state … needs to deallocate resources
  ROB/LSQ entries
  Physical register
  “colors” of various sorts
  RAT checkpoints
Most are FIFO’s or Queues
  Alloc/dealloc is usually just inc/dec head/tail pointers
Unified PRF requires a little more work
  Have to return “old” mapping to free list