## Slide 1: CSE 502: Computer Architecture
Multi-{Socket,Core,Thread}

## Slide 2: Getting More Performance
Keep pushing IPC and/or frequenecy
  Design complexity (time to market)
  Cooling (cost)
  Power delivery (cost)
  …
Possible, but too costly

## Slide 3: Bridging the Gap
IPC
100
10
1
Single-Issue
Pipelined
Superscalar
Out-of-Order
(Today)
Superscalar
Out-of-Order
(Hypothetical-
Aggressive)
Limits
Diminishing returns w.r.t.
larger instruction window,
higher issue-width
Power has been growing
exponentially as well
Watts /

## Slide 4: Higher Complexity not Worth Effort
“Effort”
Performance
Scalar
In-Order
Moderate-Pipe
Superscalar/OOO
Very-Deep-Pipe
Aggressive
Superscalar/OOO
Made sense to go
Superscalar/OOO:
good ROI
Very little gain for
substantial effort

## Slide 5: User Visible/Invisible
All performance gains up to this point were “free”
  No user intervention required (beyond buying new chip)
    Recompilation/rewriting could provide even more benefit
  Higher frequency & higher IPC
  Same ISA, different micro-architecture
Multi-processing pushes parallelism above ISA
  Coarse grained parallelism
    Provide multiple processing elements
  User (or developer) responsible for finding parallelism
    User decides how to use resources

## Slide 6: Sources of (Coarse) Parallelism
Different applications
  MP3 player in background while you work in Office
  Other background tasks: OS/kernel, virus check, etc…
  Piped applications
    gunzip -c foo.gz | grep bar | perl some-script.pl
Threads within the same application
  Java (scheduling, GC, etc...)
  Explicitly coded multi-threading
    pthreads, MPI, etc…

## Slide 7: SMP Machines
SMP = Symmetric Multi-Processing
  Symmetric = All CPUs have “equal” access to memory
OS sees multiple CPUs
  Runs one process (or thread) on each CPU
CPU0
CPU1
CPU2
CPU3

## Slide 8: MP Workload Benefits
3-wide
OOO
CPU
Task A
Task B
4-wide
OOO
CPU
Task A
Task B
Benefit
3-wide
OOO
CPU
Task A
Task B
3-wide
OOO
CPU
2-wide
OOO
CPU
Task B
Task A
2-wide
OOO
CPU
runtime
  Assumes you have multiple tasks/programs to run
Notes: Just showing that with parallelism, even two “smaller” cores may provide better overall performance than one “regular” core (and the smaller cores are likely to be cheaper from an area and power standpoint due to how these tend to grow super-linearly).

## Slide 9: … If Only One Task Available
3-wide
OOO
CPU
Task A
4-wide
OOO
CPU
Task A
Benefit
3-wide
OOO
CPU
3-wide
OOO
CPU
Task A
2-wide
OOO
CPU
2-wide
OOO
CPU
Task A
runtime
Idle
No benefit over 1 CPU
Performance
degradation!
Notes: But you’re stuck if you care about single-thread performance

## Slide 10: Benefit of MP Depends on Workload
Limited number of parallel tasks to run
  Adding more CPUs than tasks provides zero benefit
For parallel code, Amdahl’s law curbs speedup
parallelizable
1CPU
2CPUs
3CPUs
4CPUs

## Slide 11: Hardware Modifications for SMP
Processor
  Memory interface
Motherboard
  Multiple sockets (one per CPU)
  Datapaths between CPUs and memory
Other
  Case: larger (bigger motherboard, better airflow)
  Power: bigger power supply for N CPUs
  Cooling: more fans to remove N CPUs worth of heat

## Slide 12: Chip-Multiprocessing (CMP)
Simple SMP on the same chip
  CPUs now called “cores” by hardware designers
  OS designers still call these “CPUs”
Intel “Smithfield” Block Diagram
AMD Dual-Core Athlon FX

## Slide 13: On-chip Interconnects (1/5)
Today, (Core+L1+L2) = “core”
  (L3+I/O+Memory) = “uncore”
How to interconnect multiple “core”s to “uncore”?
Possible topologies
  Bus
  Crossbar
  Ring
  Mesh
  Torus
LLC $
Memory
Controller
Core
$
Core
$
Core
$
Core
$

## Slide 14: On-chip Interconnects (2/5)
Possible topologies
  Bus
  Crossbar
  Ring
  Mesh
  Torus
$
Bank 0
Memory
Controller
Core
$
Core
$
Core
$
Core
$
$
Bank 1
$
Bank 2
$
Bank 3
Oracle UltraSPARC T5 (3.6GHz, 16 cores, 8 threads per core)

## Slide 15: On-chip Interconnects (3/5)
Possible topologies
  Bus
  Crossbar
  Ring
  Mesh
  Torus
$
Bank 0
Memory
Controller
Core
$
Core
$
Core
$
Core
$
$
Bank 1
$
Bank 2
$
Bank 3
Intel Sandy Bridge (3.5GHz, 6 cores, 2 threads per core)
3 ports per switch
Simple and cheap
Can be bi-directional to reduce latency

## Slide 16: On-chip Interconnects (4/5)
Possible topologies
  Bus
  Crossbar
  Ring
  Mesh
  Torus
Tilera Tile64 (866MHz, 64 cores)
Core
$
$
Bank 1
$
Bank 0
Core
$
Core
$
$
Bank 4
Core
$
$
Bank 3
Memory
Controller
Core
$
$
Bank 2
Core
$
$
Bank 7
Core
$
$
Bank 6
Core
$
$
Bank 5
Up to 5 ports per switch
  Tiled organization combines core and cache

## Slide 17: On-chip Interconnects (5/5)
Possible topologies
  Bus
  Crossbar
  Ring
  Mesh
  Torus
5 ports per switch
Can be “folded” to avoid long links
Core
$
$
Bank 1
$
Bank 0
Core
$
Core
$
$
Bank 4
Core
$
$
Bank 3
Memory
Controller
Core
$
$
Bank 2
Core
$
$
Bank 7
Core
$
$
Bank 6
Core
$
$
Bank 5

## Slide 18: Benefits of CMP
Cheaper than multi-chip SMP
  All/most interface logic integrated on chip
    Fewer chips
    Single CPU socket
    Single interface to memory
  Less power than multi-chip SMP
    Communication on die uses less power than chip to chip
Efficiency
  Use for transistors instead of wider/more aggressive OoO
  Potentially better use of hardware resources

## Slide 19: CMP Performance vs. Power
2x CPUs not necessarily equal to 2x performance
2x CPUs  ½ power for each
  Maybe a little better than ½ if resources can be shared
Back-of-the-Envelope calculation:
  3.8 GHz CPU at 100W
  Dual-core: 50W per Core
  P  V3: Vorig3/VCMP3 = 100W/50W  VCMP = 0.8 Vorig
  f  V: fCMP = 3.0GHz
Notes: For a multi-threaded application, two 3.0GHz cores is probably better than one 3.8Ghz core.

## Slide 20: Multi-Threading
Uni-Processor: 4-6 wide, lucky if you get 1-2 IPC
  Poor utilization of transistors
SMP: 2-4 CPUs, but need independent threads
  Poor utilization as well (if limited tasks)
{Coarse-Grained,Fine-Grained,Simultaneous}-MT
  Use single large uni-processor as a multi-processor
    Core provide multiple hardware contexts (threads)
      Per-thread PC
      Per-thread ARF (or map table)
  Each core appears as multiple CPUs
    OS designers still call these “CPUs”

## Slide 21: Scalar Pipeline
Time
  Dependencies limit functional unit utilization
Notes: To motivate how we came to incorporate multithreading into EV8, let’s return to the early 1980’s and take a very high level view of instruction execution.
This very abstract diagram illustrates the activity in just the execute stage of a single issue machine, with the red boxes showing instruction execution.
Note gaps due to multiple cycle operation latency and inter-instruction dependencies which result in less than perfect utilization of the function units.

## Slide 22: Superscalar Pipeline
Time
  Higher performance than scalar, but lower utilization
Notes: If that weren’t bad enough, for more performance we now make parallel (or wide) issue to use more function units in a cycle.
Even with sophisticated techniques like out-of-order (or dynamic) issue, and sophisticated branch prediction, this leads to more waste, since there aren’t always enough instructions to issue in a cycle.
Peak sustainable execution rate – 21264 = 4, a wide variety of studies have shown this function unit unitization to be under 50%, and getting worse as machines continue to get wider.
Note I’m not saying that its bad to keep on this trajectory, because continuing to make the machine wider is still providing an absolute single stream performance benefit. Furthermore the key point is not keeping FUs busy, because they really aren’t that expensive, but because they represent more work getting done.
So what can we do….

## Slide 23: Chip Multiprocessing (CMP)
Time
  Limited utilization when running one thread
Notes: Another approach is to get more efficiency by using two smaller CPUs. But this sacrifices single stream performance. And Amdahl’s law tells us that sometimes you have parallelism and sometimes you don’t so one can’t always use multiple streams. This just means you still will see reduced function unit utilization.

## Slide 24: Coarse-Grained Multithreading (1/3)
Time
  Only good for long latency ops (i.e., cache misses)
Hardware Context Switch
Notes: Another approach is to get more efficiency by using two smaller CPUs. But this sacrifices single stream performance. And Amdahl’s law tells us that sometimes you have parallelism and sometimes you don’t so one can’t always use multiple streams. This just means you still will see reduced function unit utilization.

## Slide 25: Coarse-Grained Multithreading (2/3)
Sacrifices a little single thread performance
Tolerates only long latencies (e.g., L2 misses)
Thread scheduling policy
  Designate a “preferred” thread (e.g., thread A)
  Switch to thread B on thread A L2 miss
  Switch back to A when A L2 miss returns
Pipeline partitioning
  None, flush on switch
  Can’t tolerate latencies shorter than twice pipeline depth
  Need short in-order pipeline for good performance

## Slide 26: Coarse-Grained Multithreading (3/3)
regfile
D$
I$
B
P
regfile
thread scheduler
L2 miss?
I$
B
P
D$
original pipeline
regfile

## Slide 27: Fine-Grained Multithreading (1/3)
Time
Saturated workload → Lots of threads
Unsaturated workload → Lots of stalls
  Intra-thread dependencies still limit performance
Notes: Classic answer to problem of dependencies is to take instructions from multiple threads.
Still leaves a lot of wasted slots. Some varients of this style of multthreading result in a design where where every thread goes much slower.
I actually worked on this style of multithreading for my Ph.D ages ago, but had abandoned the idea until now.

## Slide 28: Fine-Grained Multithreading (2/3)
Sacrifices significant single-thread performance
Tolerates everything
  L2 misses
  Mispredicted branches
  etc...
Thread scheduling policy
  Switch threads often (e.g., every cycle)
  Use round-robin policy, skip threads with long-latency ops
Pipeline partitioning
  Dynamic, no flushing
  Length of pipeline doesn’t matter

## Slide 29: Fine-Grained Multithreading (3/3)
(Many) more threads
Multiple threads in pipeline at once
thread scheduler
regfile
regfile
regfile
regfile
I$
B
P
D$

## Slide 30: Simultaneous Multithreading (1/3)
Time
  Max utilization of functional units
Notes: What changed my mind was the work by Dean Tullsen at U. Washington who addressed waste issue, by proposing simultaneous multithreading.
What he suggested was simply using any available slot for any available thread.
But his work was somewhat incomplete, so we then collaborated to work on achieving the goal of uncompromsed single stream performance - and multithreading...

## Slide 31: Simultaneous Multithreading (2/3)
Tolerates all latencies
Sacrifices some single thread performance
Thread scheduling policy
  Round-robin (like Fine-Grained MT)
Pipeline partitioning
  Dynamic
Examples
  Pentium4 (hyper-threading): 5-way issue, 2 threads
  Alpha 21464: 8-way issue, 4 threads (canceled)

## Slide 32: Simultaneous Multithreading (3/3)
regfile
D$
I$
B
P
map table
map tables
thread scheduler
original pipeline
I$
B
P
regfile
D$

## Slide 33: Issues for SMT
Cache interference
  Concern for all MT variants
  Shared memory SPMD threads help here
    Same insns.  share I$
    Shared data  less D$ contention
    MT is good for “server” workloads
  SMT might want a larger L2 (which is OK)
    Out-of-order tolerates L1 misses
Large map table and physical register file
  #maptable-entries = (#threads * #arch-regs)
  #phys-regs = (#threads * #arch-regs) + #in-flight insns

## Slide 34: Latency vs. Throughput
MT trades (single-thread) latency for throughput
  Sharing processor degrades latency of individual threads
  But improves aggregate latency of both threads
  Improves utilization
Example
  Thread A: individual latency=10s, latency with thread B=15s
  Thread B: individual latency=20s, latency with thread A=25s
  Sequential latency (first A then B or vice versa): 30s
  Parallel latency (A and B simultaneously): 25s
  MT slows each thread by 5s
  But improves total latency by 5s
  Benefits of MT depend on workload

## Slide 35: CMP vs. MT
If you wanted to run multiple threads would you build a…
  Chip multiprocessor (CMP): multiple separate pipelines?
  A multithreaded processor (MT): a single larger pipeline?
Both will get you throughput on multiple threads
  CMP will be simpler, possibly faster clock
  SMT will get you better performance (IPC) on a single thread
    SMT is basically an ILP engine that converts TLP to ILP
    CMP is mainly a TLP engine
Do both (CMP of MTs), Example: Sun UltraSPARC T1
  8 processors, each with 4-threads (fine-grained threading)
  1GHz clock, in-order, short pipeline
  Designed for power-efficient “throughput computing”

## Slide 36: Combining MP Techniques (1/2)
System can have SMP, CMP, and SMT at the same time
Example machine with 32 threads
  Use 2-socket SMP motherboard with two chips
  Each chip with an 8-core CMP
  Where each core is 2-way SMT
Makes life difficult for the OS scheduler
  OS needs to know which CPUs are…
    Real physical processor (SMP): highest independent performance
    Cores in same chip: fast core-to-core comm., but shared resources
    Threads in same core: competing for resources
  Distinct apps. scheduled on different CPUs
  Cooperative apps. (e.g., pthreads) scheduled on same core
  Use SMT as last choice (or don’t use for some apps.)

## Slide 37: Combining MP Techniques (2/2)

## Slide 38: Scalability Beyond the Machine

## Slide 39: Server Racks

## Slide 40: Datacenters (1/2)

## Slide 41: Datacenters (2/2)