## Slide 1: CSE 502: Computer Architecture
Shared-Memory Multi-Processors

## Slide 2: Shared-Memory Multiprocessors
Multiple threads use shared memory (address space)
  “SysV Shared Memory” or “Threads” in software
Communication implicit via loads and stores
  Opposite of explicit message-passing multiprocessors
Theoretical foundation: PRAM model
P1
P2
P3
P4
Memory System
Notes: Familiar for system (OS and DB) as well as application programmers
  Why? The same techniques that use concurrency to overlap disk and network latencies also work for parallel speedup on MPs. The exact same software can take advantage of MPs with only small changes

## Slide 3: Why Shared Memory?
Pluses
  App sees multitasking uniprocessor
  OS needs only evolutionary extensions
  Communication happens without OS
Minuses
  Synchronization is complex
  Communication is implicit (hard to optimize)
  Hard to implement (in hardware)
Result
  SMPs and CMPs are most successful machines to date
  First with multi-billion-dollar markets

## Slide 4: Paired vs. Separate Processor/Memory?
Separate CPU/memory
  Uniform memory access (UMA)
    Equal latency to memory
  Low peak performance
Paired CPU/memory
  Non-uniform memory access (NUMA)
    Faster local memory
    Data placement matters
  High peak performance
CPU($)
Mem
CPU($)
Mem
CPU($)
Mem
CPU($)
Mem
CPU($)
Mem
CPU($)
Mem
CPU($)
Mem
CPU($)
Mem
R
R
R
R

## Slide 5: Shared vs. Point-to-Point Networks
Shared network
  Example: bus
  Low latency
  Low bandwidth
    Doesn’t scale >~16 cores
  Simple cache coherence
Point-to-point network:
  Example: mesh, ring
  High latency (many “hops”)
  Higher bandwidth
    Scales to 1000s of cores
  Complex cache coherence
CPU($)
Mem
CPU($)
Mem
R
CPU($)
Mem
R
CPU($)
Mem
R
CPU($)
Mem
R
CPU($)
Mem
CPU($)
Mem
CPU($)
Mem
R
R
R
R

## Slide 6: Organizing Point-To-Point Networks
Network topology: organization of network
  Trade off perf. (connectivity, latency, bandwidth)  cost
Router chips
  Networks w/separate router chips are indirect
  Networks w/ processor/memory/router in chip are direct
    Fewer components, “Glueless MP”
CPU($)
Mem
CPU($)
Mem
CPU($)
Mem
CPU($)
Mem
R
R
R
R
R
R
R
CPU($)
Mem
R
CPU($)
Mem
R
CPU($)
Mem
R
CPU($)
Mem
R

## Slide 7: Issues for Shared Memory Systems
Two big ones
  Cache coherence
  Memory consistency model
Closely related
Often confused

## Slide 8: Cache Coherence: The Problem (1/2)
A: 0
Variable A initially has value 0
P1 stores value 1 into A
P2 loads A from memory and sees old value 0
Bus
P1
t1: Store A=1
P2
A: 0
A: 0 1
A: 0
Main Memory
L1
t2: Load A?
L1
  Need to do something to keep P2’s cache coherent

## Slide 9: Cache Coherence: The Problem (2/2)
A: 0
P1 and P2 have variable A (value 0) in their caches
P1 stores value 1 into A
P2 loads A from its cache and sees old value 0
Bus
P1
t1: Store A=1
P2
A: 0
A: 0 1
A: 0
Main Memory
L1
t2: Load A?
L1
  Need to do something to keep P2’s cache coherent

## Slide 10: Approaches to Cache Coherence
Software-based solutions
  Mechanisms:
    Mark cache blocks/memory pages as cacheable/non-cacheable
    Add “Flush” and “Invalidate” instructions
  Could be done by compiler or run-time system
  Difficult to get perfect (e.g., what about memory aliasing?)
Hardware solutions are far more common
  System ensures everyone always sees the latest value

## Slide 11: Coherence with Write-through Caches
Allows multiple readers, but writes through to bus
  Requires Write-through, no-write-allocate cache
All caches must monitor (aka “snoop”) all bus traffic
  Simple state machine for each cache frame
Bus
P1
t1: Store A=1
P2
A: 0
A [V]: 0
A [V]: 0
Main Memory
Write-through
No-write-allocate
t2: BusWr A=1
t3: Invalidate A
A [V I]: 0
A: 0 1
A [V]: 0 1

## Slide 12: Valid-Invalid Snooping Protocol
Processor Actions
  Ld, St, BusRd, BusWr
Bus Messages
  BusRd, BusWr
Track 1 bit per cache frame
  Valid/Invalid
Store / BusWr
BusWr / --
Store / BusWr
Load / BusRd
Load / --
Valid
Invalid
Notes: 9

## Slide 13: Supporting Write-Back Caches
Write-back caches are good
  Drastically reduce bus write bandwidth
Add notion of “ownership” to Valid-Invalid
  When “owner” has only replica of a cache block
    Update it freely
  Multiple readers are ok
    Not allowed to write without gaining ownership
  On a read, system must check if there is an owner
    If yes, take away ownership

## Slide 14: Modified-Shared-Invalid (MSI) States
Processor Actions
  Load, Store, Evict
Bus Messages
  BusRd, BusRdX, BusInv, BusWB, BusReply (Here for simplicity, some messages can be combined)
Track 3 states per cache frame
  Invalid: cache does not have a copy
  Shared: cache has a read-only copy; clean
    Clean: memory (or later caches) is up to date
  Modified: cache has the only valid copy; writable; dirty
    Dirty: memory (or later caches) is out of date

## Slide 15: Simple MSI Protocol (1/9)
Invalid
Load / BusRd
Shared
Bus
A [I]
A: 0
P2
A [I]
P1
1: Load A
2: BusRd A
3: BusReply A
A [I S]: 0
Notes: 9

## Slide 16: Simple MSI Protocol (2/9)
Invalid
Load / BusRd
Shared
Load / --
BusRd / [BusReply]
Bus
A [I]
A: 0
P2
A [S]: 0
P1
1: Load A
2: BusRd A
3: BusReply A
1: Load A
A [I S]: 0
Notes: 9

## Slide 17: Simple MSI Protocol (3/9)
Invalid
Load / BusRd
Shared
Load / --
BusRd / [BusReply]
Evict / --
Bus
A [I]
A: 0
P2
A [S]: 0
P1
A [S]: 0
A [S I]
Evict A
Notes: 9

## Slide 18: Simple MSI Protocol (4/9)
A [S]: 0
Store / BusRdX
Invalid
Load / BusRd
Shared
Load / --
BusRd / [BusReply]
Modified
Evict / --
BusRdX / [BusReply]
Bus
A [I]
A: 0
P2
A [S I]: 0
P1
1: Store A
2: BusRdX A
3: BusReply A
A [I M]: 0 1
Load, Store / --
Notes: 9

## Slide 19: Simple MSI Protocol (5/9)
Store / BusRdX
Invalid
Load / BusRd
Shared
Load / --
BusRd / [BusReply]
Modified
Evict / --
BusRd / BusReply
Load, Store / --
BusRdX / [BusReply]
Bus
A [M]: 1
A: 0
P2
A [I]
P1
1: Load A
2: BusRd A
3: BusReply A
A [I S]: 1
A [M S]: 1
A: 0 1
4: Snarf A
Notes: 9

## Slide 20: Simple MSI Protocol (6/9)
Store / BusRdX
Invalid
Load / BusRd
Shared
Load / --
BusRd / [BusReply]
Modified
Evict / --
BusRd / BusReply
Load, Store / --
Store / BusInv
Bus
A [S]: 1
A: 1
P2
A [S]: 1
P1
1: Store A
aka “Upgrade”
2: BusInv A
A [S M]: 2
A [S I]
BusRdX / [BusReply]
BusRdX, BusInv / [BusReply]
Notes: 9

## Slide 21: Simple MSI Protocol (7/9)
Store / BusRdX
Invalid
Load / BusRd
Shared
Load / --
BusRd / [BusReply]
Modified
BusRdX / BusReply
Evict / --
BusRd / BusReply
Load, Store / --
Store / BusInv
BusRdX, BusInv / [BusReply]
Bus
A [I]
A: 1
P2
A [M]: 2
P1
1: Store A
2: BusRdX A
3: BusReply A
A [M I]: 2
A [I M]: 3
Notes: 9

## Slide 22: Simple MSI Protocol (8/9)
Store / BusRdX
Invalid
Load / BusRd
Shared
Load / --
BusRd / [BusReply]
Modified
BusRdX / BusReply
Evict / --
BusRd / BusReply
Evict / BusWB
Load, Store / --
Store / BusInv
BusRdX, BusInv / [BusReply]
Bus
A [M]: 3
A: 1
P2
A [I]
P1
1: Evict A
2: BusWB A
A [M I]: 3
A: 1 3
Notes: 9

## Slide 23: Simple MSI Protocol (9/9)
Store / BusRdX
Invalid
Load / BusRd
Shared
Load / --
BusRd / [BusReply]
Cache Actions:
Load, Store, Evict
Bus Actions:
BusRd, BusRdX BusInv, BusWB, BusReply
Modified
BusRdX / BusReply
Evict / --
BusRd / BusReply
Evict / BusWB
Load, Store / --
Store / BusInv
BusRdX, BusInv / [BusReply]
  Usable coherence protocol
Notes: 9

## Slide 24: Scalable Cache Coherence
Part I: bus bandwidth
  Replace non-scalable bandwidth substrate (bus) …with scalable-bandwidth one (e.g., mesh)
Part II: processor snooping bandwidth
  Most snoops result in no action
  Replace non-scalable broadcast protocol (spam everyone) …with scalable directory protocol (spam cores that care)
  Requires a “directory” to keep track of “sharers”

## Slide 25: Directory Coherence Protocols
Extend memory to track caching information
For each physical cache line, a home directory tracks:
  Owner: core that has a dirty copy (i.e., M state)
  Sharers: cores that have clean copies (i.e., S state)
Cores send coherence events to home directory
  Home directory only sends events to cores that care

## Slide 26: Read Transaction
L has a cache miss on a load instruction
L
H
1: Read Req
2: Read Reply

## Slide 27: 4-hop Read Transaction
L has a cache miss on a load instruction
  Block was previously in modified state at R
L
H
1: Read Req
4: Read Reply
R
State: M Owner: R
2: Recall Req
3: Recall Reply

## Slide 28: 3-hop Read Transaction
L has a cache miss on a load instruction
  Block was previously in modified state at R
L
H
1: Read Req
3: Read Reply
R
State: M Owner: R
2: Fwd’d Read Req
3: Fwd’d Read Ack

## Slide 29: An Example Race: Writeback & Read
L has dirty copy, wants to write back to H
R concurrently sends a read to H
H
1: WB Req
5: Read Reply
R
State: M Owner: L
2: Read Req
3: Fwd’d Read Req
4:
Race ! WB & Fwd Rd
No need to ack
6:
Race!
Final State: S
No need to Ack
  Races require complex intermediate states
L

## Slide 30: Basic Operation: Read
Read A (miss)
#1
Directory
#2
Read A
Fill A
A: Shared, #1
  Typical way to reason about directories

## Slide 31: Basic Operation: Write
Read A (miss)
Read A
Fill A
A: Shared, #1
ReadExclusive A
Invalidate A
Fill A
Inv Ack A
A: Mod., #2
#1
Directory
#2

## Slide 32: Coherence vs. Consistency
Coherence concerns only one memory location
Consistency concerns ordering for all locations
A Memory System is Coherent if
  Can serialize all operations to that location
    Operations performed by any core appear in program order
  Read returns value written by last store to that location
A Memory System is Consistent if
  It follows the rules of its Memory Model
    Operations on memory locations appear in some defined order
Notes: 3

## Slide 33: Why Coherence != Consistency
/* initial A = B = flag = 0 */
P1 P2
A = 1; while (flag == 0); /* spin */
B = 1; print A;
flag = 1; print B;
Intuition says we see “1” printed twice (A,B)
Coherence doesn’t say anything
  Different memory locations
Uniprocessor ordering (LSQ) won’t help
  Consistency defines what is “correct” behavior
Notes: 4

## Slide 34: Sequential Consistency (SC)
switch randomly set
after each memory op
processors
issue memory ops
in program order
P1
P2
P3
Memory
  Defines Single Sequential Order Among All Ops.
Notes: 5

## Slide 35: Sufficient Conditions for SC
“A multiprocessor is sequentially consistent if the result of any execution is the same as if the operations of all the processors were executed in some sequential order, and the operations of each individual processor appear in this sequence in the order specified by its program.”
-Lamport, 1979
Every proc. issues memory ops in program order
Memory ops happen (start and end) atomically
  On Store, wait to commit before issuing next memory op
  On Load, wait to write back before issuing next op
  Easy to reason about, very slow (without ugly tricks)
Notes: 6

## Slide 36: Mutual Exclusion Example
Mutually exclusive access to a critical region
  Works as advertised under Sequential Consistency
  Fails if P1 and P2 see different Load/Store order
    OoO allows P1 to read B before writing (committing) A
P1 P2
lockA: A = 1; lockB: B=1;
if (B != 0) if (A != 0)
{ A = 0; goto lockA; } { B = 0; goto lockB; }
/* critical section*/ /* critical section*/ A = 0; B = 0;
Notes: 4

## Slide 37: Problems with SC Memory Model
Difficult to implement efficiently in hardware
  Straight-forward implementations:
    No concurrency among memory access
    Strict ordering of memory accesses at each node
    Essentially precludes out-of-order CPUs
Unnecessarily restrictive
  Most parallel programs won’t notice out-of-order accesses
Conflicts with latency hiding techniques
Notes: 3

## Slide 38: Mutex Example w/ Store Buffer
P1 P2
lockA: A = 1; lockB: B=1;
if (B != 0) if (A != 0)
{ A = 0; goto lockA; } { B = 0; goto lockB; }
/* critical section*/ /* critical section*/ A = 0; B = 0;
Shared Bus
P1
Read B
t1
t3
P2
Read A
t2
t4
A: 0
B: 0
Write A
Write B
  Does not work

## Slide 39: Relaxed Consistency Models
Sequential Consistency (SC):
  R → W, R → R, W → R, W → W
Total Store Ordering (TSO) relaxes W → R
  R → W, R → R, W → W
Partial Store Ordering relaxes W → W (coalescing WB)
  R → W, R → R
Weak Ordering or Release Consistency (RC)
  All ordering explicitly declared
    Use fences to define boundaries
    Use acquire and release to force flushing of values
X → Y
X must complete before Y

## Slide 40: Atomic Operations & Synchronization
Atomic operations perform multiple actions together
  Each of these can implement the others
Compare-and-Swap (CAS)
  Compare memory value to arg1, write arg2 on match
Test-and-Set
  Overwrite memory value with arg1 and return old value
Fetch-and-Increment
  Increment value in memory and return the old value
Load-Linked/Store-Conditional (LL/SC)
  Two operations, but Store succeeds iff value unchanged