## Slide 1: CSE 502: Computer Architecture
Core Pipelining

## Slide 2: Generic Instruction Cycle
Steps in processing an instruction:
  Instruction Fetch (IF_STEP)
  Instruction Decode (ID_STEP)
  Operand Fetch (OF_STEP)
  Execute (EX_STEP)
  Result Store or Write Back (RS_STEP)
Actions per instruction at each stage given by ISA
μArch determines how HW implements the steps

## Slide 3: Prototypical Processor Organization
Issue
Decode
Memory
Execute
Addr-gen.
Fetch
Instruction
Access
Register
File
PC
+4
Data
Access
ALU
(Write-back)

## Slide 4: Datapath vs. Control Logic
Datapath is HW components and connections
  Determines the static structure of processor
Control logic controls data flow in datapath
  Control is determined by
    Instruction words
    State of the processor
    Execution results at each stage

## Slide 5: Single-Instruction Datapath
Process one instruction at a time
Single-cycle control: hardwired
  Low CPI (1)
  Long clock period (to accommodate slowest instruction)
Multi-cycle control: typically micro-programmed
  Short clock period
  High CPI
Can we have both low CPI and short clock period?
  Not if datapath executes only one instruction at a time
  No good way to make a single instruction go faster
Single-cycle
Multi-cycle
ins0.(fetch,dec,ex,mem,wb)
ins1.(fetch,dec,ex,mem,wb)
ins0.(dec,ex)
ins0.fetch
ins1.(dec,ex)
ins1.fetch
ins0.(mem,wb)
ins1.(mem,wb)
time

## Slide 6: Pipelined Datapath
Start with multi-cycle design
When insn0 goes from stage 1 to stage 2 … insn1 starts stage 1
Each instruction passes through all stages … but instructions enter and leave at faster rate
  Pipeline can have as many insns in flight as there are stages
Multi-cycle
ins0.(dec,ex)
ins0.fetch
ins1.(dec,ex)
ins1.fetch
ins0.(mem,wb)
ins1.(mem,wb)
time
Pipelined
ins0.(mem,wb)
ins0.(dec,ex)
ins0.fetch
ins1.(dec,ex)
ins1.fetch
ins1.(mem,wb)
ins2.(dec,ex)
ins2.fetch
ins2.(mem,wb)
Style | Ideal CPI | Cycle Time (1/freq)
Single-cycle | 1 | Long
Multi-cycle | > 1 | Short
Pipelined | 1 | Short

## Slide 7: Pipeline Examples
Stage delay =
Bandwidth =
Stage delay =
Bandwidth =
Stage delay =
Bandwidth =
address
hit?
=
=
=
=
  Increases throughput at the expense of latency
address
hit?
=
=
=
=
address
hit?
=
=
=
=

## Slide 8: 5-Stage MIPS Datapath
Write-Back (WB)
Memory
(MEM)
Execute
(EX)
Inst. Decode &
Register Read
(ID)
Inst. Fetch
(IF)
I-cache
Reg
File
PC
+1
D-cache
ALU
RS_STEP
IF_STEP
ID_STEP
OF_STEP
EX_STEP

## Slide 9: Stage 1: Fetch
Fetch instruction from instruction cache
  Use PC to index instruction cache
  Increment PC (assume no branches for now)
Write state to the pipeline register (IF/ID)
  The next stage will read this pipeline register

## Slide 10: Stage 1: Fetch Diagram
Instruction
bits
IF / ID
Pipeline register
PC
Instruction
Cache
en
en
1
+
M
U
X
PC + 1
Decode
target

## Slide 11: Stage 2: Decode
Decodes opcode bits
  Set up Control signals for later stages
Read input operands from register file
  Specified by decoded instruction bits
Write state to the pipeline register (ID/EX)
  Opcode
  Register contents, immediate operand
  PC+1 (even though decode didn’t use it)
  Control signals (from insn) for opcode and destReg

## Slide 12: Stage 2: Decode Diagram
ID / EX
Pipeline register
regA
contents
regB
contents
Register File
regA
regB
en
Instruction
bits
IF / ID
Pipeline register
PC + 1
PC + 1
Control
Signals/imm
Fetch
Execute
destReg
data
target

## Slide 13: Stage 3: Execute
Perform ALU operations
  Calculate result of instruction
    Control signals select operation
    Contents of regA used as one input
    Either regB or constant offset (imm from insn) used as second input
  Calculate PC-relative branch target
    PC+1+(constant offset)
Write state to the pipeline register (EX/Mem)
  ALU result, contents of regB, and PC+1+offset
  Control signals (from insn) for opcode and destReg

## Slide 14: Stage 3: Execute Diagram
ID / EX
Pipeline register
regA
contents
regB
contents
EX/Mem
Pipeline register
PC + 1
Control
Signals/imm
Control
Signals
PC+1
+offset
+
regB
contents
Decode
Memory
destReg
data
target
A
L
U
M
U
X
ALU
result

## Slide 15: Stage 4: Memory
Perform data cache access
  ALU result contains address for LD or ST
  Opcode bits control R/W and enable signals
Write state to the pipeline register (Mem/WB)
  ALU result and Loaded data
  Control signals (from insn) for opcode and destReg

## Slide 16: Stage 4: Memory Diagram
ALU
result
Mem/WB
Pipeline register
ALU
result
EX/Mem
Pipeline register
Control
signals
PC+1
+offset
regB
contents
Loaded
data
Data Cache
en R/W
in_addr
in_data
Control
signals
Execute
Write-back
destReg
data
target

## Slide 17: Stage 5: Write-back
Writing result to register file (if required)
  Write Loaded data to destReg for LD
  Write ALU result to destReg for ALU insn
  Opcode bits control register write enable signal

## Slide 18: Stage 5: Write-back Diagram
ALU
result
Mem/WB
Pipeline register
Control
signals
Loaded
data
M
U
X
data
destReg
M
U
X
Memory

## Slide 19: Putting It All Together
PC
Inst
Cache
Register
File
M
U
X
A
L
U
1
Data
Cache
+
+
M
U
X
IF/ID
ID/EX
EX/Mem
Mem/WB
M
U
X
Control
signals/imm
valB
valA
PC+1
PC+1
target
ALU
result
Control
signals
valB
ALU
result
mdata
eq?
instruction
regA
regB
data
dest
M
U
X
data
dest
Control
signals

## Slide 20: Pipelining Idealism
Uniform Sub-operations
  Operation can partitioned into uniform-latency sub-ops
Repetition of Identical Operations
  Same ops performed on many different inputs
Independent Operations
  All ops are mutually independent

## Slide 21: Pipeline Realism
Uniform Sub-operations … NOT!
  Balance pipeline stages
    Stage quantization to yield balanced stages
    Minimize internal fragmentation (left-over time near end of cycle)
Repetition of Identical Operations … NOT!
  Unifying instruction types
    Coalescing instruction types into one “multi-function” pipe
    Minimize external fragmentation (idle stages to match length)
Independent Operations … NOT!
  Resolve data and resource hazards
    Inter-instruction dependency detection and resolution
  Pipelining is expensive

## Slide 22: The Generic Instruction Pipeline
Instruction Fetch
Instruction Decode
Operand Fetch
Instruction Execute
Write-back
IF
ID
OF
EX
WB

## Slide 23: Balancing Pipeline Stages
  Can we do better?
TIF= 6 units
TID= 2 units
TID= 9 units
TEX= 5 units
TOS= 9 units
Without pipelining
Tcyc TIF+TID+TOF+TEX+TOS
= 31
Pipelined
Tcyc  max{TIF, TID, TOF, TEX, TOS}
= 9
Speedup = 31 / 9 = 3.44
IF
ID
OF
EX
WB

## Slide 24: Balancing Pipeline Stages (1/2)
Two methods for stage quantization
  Divide sub-ops into smaller pieces
  Merge multiple sub-ops into one
Recent/Current trends
  Deeper pipelines (more and more stages)
  Pipelining of memory accesses
  Multiple different pipelines/sub-pipelines

## Slide 25: Balancing Pipeline Stages (2/2)
Coarser-Grained Machine Cycle: 4 machine cyc / instruction
Finer-Grained Machine Cycle: 11 machine cyc /instruction
TIF&ID= 8 units
TOF= 9 units
TEX= 5 units
TOS= 9 units
IF
ID
OF
WB
EX
# stages = 11
Tcyc= 3 units
IF
IF
ID
OF
OF
OF
EX
EX
WB
WB
WB
# stages = 4
Tcyc= 9 units

## Slide 26: Pipeline Examples
IF
RD
ALU
MEM
WB
IF_STEP
ID_STEP
OF_STEP
EX_STEP
RS_STEP
PC GEN
Cache Read
Cache Read
Decode
Read REG
Addr GEN
Cache Read
Cache Read
EX 1
EX 2
Check Result
Write Result
MIPS R2000/R3000
AMDAHL 470V/7
IF_STEP
ID_STEP
OF_STEP
EX_STEP
RS_STEP

## Slide 27: Instruction Dependencies (1/2)
Data Dependence
  Read-After-Write (RAW) (the only true dependence)
    Read must wait until earlier write finishes
  Anti-Dependence (WAR)
    Write must wait until earlier read finishes (avoid clobbering)
  Output Dependence (WAW)
    Earlier write can’t overwrite later write
Control Dependence (a.k.a. Procedural Dependence)
  Branch condition must execute before branch target
  Instructions after branch cannot run before branch

## Slide 28: Instruction Dependencies (1/2)
  Real code has lots of dependencies
  # for ( ; (j < high) && (array[j] < array[low]); ++j);
  bge j, high, L2
  mul $15, j, 4
  addu $24, array, $15
  lw $25, 0($24)
  mul $13, low, 4
  addu $14, array, $13
  lw $15, 0($14)
  bge $25, $15, L2
L1:
  addu j, j, 1
  . . .
L2:
  addu $11, $11, -1
  . . .
From
Quicksort:

## Slide 29: Hardware Dependency Analysis
Processor must handle
  Register Data Dependencies (same register)
    RAW, WAW, WAR
  Memory Data Dependencies (same address)
    RAW, WAW, WAR
  Control Dependencies

## Slide 30: Pipeline Terminology
Pipeline Hazards
  Potential violations of program dependencies
    Due to multiple in-flight instructions
  Must ensure program dependencies are not violated
Hazard Resolution
  Static method: compiler guarantees correctness
    By inserting No-Ops or independent insns between dependent insns
  Dynamic method: hardware checks at runtime
    Two basic techniques: Stall (costs perf.), Forward (costs hw)
Pipeline Interlock
  Hardware mechanism for dynamic hazard resolution
  Must detect and enforce dependencies at runtime

## Slide 31: Pipeline: Steady State
IF
ID
RD
ALU
MEM
WB
IF
ID
RD
ALU
MEM
WB
IF
ID
RD
ALU
MEM
WB
IF
ID
RD
ALU
MEM
WB
IF
ID
RD
ALU
MEM
WB
IF
ID
RD
ALU
MEM
IF
ID
RD
ALU
IF
ID
RD
IF
ID
IF
t0
t1
t2
t3
t4
t5
Instj
Instj+1
Instj+2
Instj+3
Instj+4

## Slide 32: Data Hazards
Necessary conditions:
  WAR: write stage earlier than read stage
    Is this possible in IF-ID-RD-EX-MEM-WB?
  WAW: write stage earlier than write stage
    Is this possible in IF-ID-RD-EX-MEM-WB?
  RAW: read stage earlier than write stage
    Is this possible in IF-ID-RD-EX-MEM-WB?
If conditions not met, no need to resolve
Check for both register and memory

## Slide 33: Pipeline: Data Hazard
Only RAW in our case
How to detect?
  Compare read register specifiers for newer instructions with write register specifiers for older instructions
t0
t1
t2
t3
t4
t5
IF
ID
RD
ALU
MEM
WB
IF
ID
RD
ALU
MEM
WB
IF
ID
RD
ALU
MEM
WB
IF
ID
RD
ALU
MEM
WB
IF
ID
RD
ALU
MEM
WB
IF
ID
RD
ALU
MEM
IF
ID
RD
ALU
IF
ID
RD
IF
ID
IF
Instj
Instj+1
Instj+2
Instj+3
Instj+4

## Slide 34: Option 1: Stall on Data Hazard
Instructions in IF and ID stay
IF/ID pipeline latch not updated
Send no-op down pipeline (called a bubble)
IF
ID
RD
ALU
MEM
WB
IF
ID
RD
ALU
MEM
WB
IF
ID
Stalled in RD
ALU
MEM
WB
IF
Stalled in ID
RD
ALU
MEM
WB
Stalled in IF
ID
RD
ALU
MEM
IF
ID
RD
ALU
t0
t1
t2
t3
t4
t5
RD
ID
IF
IF
ID
RD
IF
ID
IF
Instj
Instj+1
Instj+2
Instj+3
Instj+4

## Slide 35: Option 2: Forwarding Paths (1/3)
IF
ID
RD
ALU
MEM
WB
IF
ID
RD
ALU
MEM
WB
IF
ID
RD
ALU
MEM
WB
IF
ID
RD
ALU
MEM
WB
IF
ID
RD
ALU
MEM
WB
IF
ID
RD
ALU
MEM
IF
ID
RD
ALU
IF
ID
RD
IF
ID
IF
t0
t1
t2
t3
t4
t5
Many possible paths
Instj
Instj+1
Instj+2
Instj+3
Instj+4
MEM
ALU
Requires stalling even with forwarding paths

## Slide 36: Option 2: Forwarding Paths (2/3)
ALU
MEM
WB
IF
src1
src2
dest
ID
Register File

## Slide 37: Option 2: Forwarding Paths (3/3)
Deeper pipelines in general require additional forwarding paths
IF
Register File
src1
src2
ALU
MEM
dest
=
=
=
=
WB
=
=
ID

## Slide 38: Pipeline: Control Hazard
t0
t1
t2
t3
t4
t5
Insti
Insti+1
Insti+2
Insti+3
Insti+4
IF
ID
RD
ALU
MEM
WB
IF
ID
RD
ALU
MEM
WB
IF
ID
RD
ALU
MEM
WB
IF
ID
RD
ALU
MEM
WB
IF
ID
RD
ALU
MEM
WB
IF
ID
RD
ALU
MEM
IF
ID
RD
ALU
IF
ID
RD
IF
ID
IF
Note: The target of Insti+1 is available at the end of the ALU stage, but it takes one more cycle (MEM) to be written to the PC register

## Slide 39: Option 1: Stall on Control Hazard
Stop fetching until branch outcome is known
  Send no-ops down the pipe
Easy to implement
Performs poorly
  ~1 of 6 instructions are branches
  Each branch takes 4 cycles
  CPI = 1 + 4 x 1/6 = 1.67 (lower bound)
IF
ID
RD
ALU
MEM
WB
IF
ID
RD
ALU
MEM
WB
IF
ID
RD
ALU
MEM
IF
ID
RD
ALU
IF
ID
RD
IF
ID
IF
t0
t1
t2
t3
t4
t5
Insti
Insti+1
Insti+2
Insti+3
Insti+4
Stalled in IF

## Slide 40: Option 2: Prediction for Control Hazards
Predict branch not taken
Send sequential instructions down pipeline
Must stop memory and RF writes
Kill instructions later if incorrect; we would know at the end of ALU
Fetch from branch target
t0
t1
t2
t3
t4
t5
Insti
Insti+1
Insti+2
Insti+3
Insti+4
IF
ID
RD
ALU
MEM
WB
IF
ID
RD
ALU
MEM
WB
IF
ID
RD
ALU
nop
nop
IF
ID
RD
nop
nop
IF
ID
nop
nop
IF
ID
RD
IF
ID
IF
nop
nop
nop
ALU
nop
RD
ALU
ID
RD
nop
nop
nop
New Insti+2
New Insti+3
New Insti+4
Speculative State Cleared
Fetch Resteered

## Slide 41: Option 3: Delay Slots for Control Hazards
Another option: delayed branches
  # of delay slots (ds) : stages between IF and where the branch is resolved
    3 in our example
  Always execute following ds instructions
  Put useful instruction there, otherwise no-op
Losing popularity
  Just a stopgap (one cycle, one instruction)
  Superscalar processors (later)
    Delay slot just gets in the way (special case)
Legacy from old RISC ISAs

## Slide 42: Going Beyond Scalar
Scalar pipeline limited to CPI ≥ 1.0
  Can never run more than 1 insn per cycle
“Superscalar” can achieve CPI ≤ 1.0 (i.e., IPC ≥ 1.0)
  Superscalar means executing multiple insns in parallel

## Slide 43: Architectures for Instruction Parallelism
Scalar pipeline (baseline)
  Instruction overlap parallelism = D
  Operation Latency = 1
  Peak IPC = 1.0
D
Successive
Instructions
Time in cycles
1
2
3
4
5
6
7
8
9
10
11
12
D different instructions overlapped

## Slide 44: Superscalar Machine
Superscalar (pipelined) Execution
  Instruction parallelism = D x N
  Operation Latency = 1
  Peak IPC = N per cycle
Successive
Instructions
Time in cycles
1
2
3
4
5
6
7
8
9
10
11
12
N
D x N different instructions overlapped

## Slide 45: Superscalar Example: Pentium
Prefetch
Decode1
Decode2
Decode2
Execute
Execute
Writeback
Writeback
4× 32-byte buffers
Decode up to 2 insts
Read operands, Addr comp
Asymmetric pipes
u-pipe
v-pipe
shift
rotate
some FP
jmp, jcc,
call,
fxch
both
mov, lea,
simple ALU,
push/pop
test/cmp

## Slide 46: Pentium Hazards & Stalls
“Pairing Rules” (when can’t two insns exec?)
  Read/flow dependence
    mov eax, 8
    mov [ebp], eax
  Output dependence
    mov eax, 8
    mov eax, [ebp]
  Partial register stalls
    mov al, 1
    mov ah, 0
  Function unit rules
    Some instructions can never be paired
      MUL, DIV, PUSHA, MOVS, some FP

## Slide 47: Limitations of In-Order Pipelines
If the machine parallelism is increased
  … dependencies reduce performance
  CPI of in-order pipelines degrades sharply
    As N approaches avg. distance between dependent instructions
    Forwarding is no longer effective
  Must stall often
  In-order pipelines are rarely full

## Slide 48: The In-Order N-Instruction Limit
On average, parent-child separation is about 5 insn
  (Franklin and Sohi ’92)
  Reasonable in-order superscalar is effectively N=2
Ex. Superscalar degree N = 4
Any dependency
between these
instructions will
cause a stall
Dependent insn
must be N = 4
instructions away
Average of 5 means there are many cases when the separation is < 4… each of these limits parallelism