## Slide 1: SystemVerilog

## Slide 2: First Things First
SystemVerilog is a superset of Verilog
  The subset we use is 99% Verilog + a few new constructs
  Familiarity with Verilog (or even VHDL) helps a lot
SystemVerilog resources on “Assignments” page
  Including a link to a good Verilog tutorial

## Slide 3: Hardware Description Languages
Used for a variety of purposes in hardware design
  High-level behavioral modeling
  Register Transfer Level (RTL) behavioral modeling
  Gate and transistor level netlists
  Timing models for timing simulation
  Design verification and testbench development
  …
Many different features to accommodate all of these
We focus on RTL modeling for the course project
  Much simpler than designing with gates
  Still helps you think like a hardware designer

## Slide 4: HDLs vs. Programming Languages
Have syntactically similar constructs:
  Data types, variables, assignments, if statements, loops, …
But very different mentality and semantic model: everything runs in parallel, unless specified otherwise
  Statements model hardware
  Hardware is inherently parallel
Software programs are composed of subroutines (mostly)
  Subroutines call each other
  When in a callee, the caller’s execution is paused
Hardware descriptions are composed of modules (mostly)
  A hierarchy of modules connected to each other
  Modules are active at the same time

## Slide 5: Modules
The basic building block in SystemVerilog
  Interfaces with outside using ports
  Ports are either input or output (for now)
module mymodule(a, b, c, f);
output f;
input a, b, c;
// Description goes here
endmodule
// alternatively
module mymodule(input a, b, c, output f);
// Description goes here
endmodule
all ports declared here
declare which ports are inputs, which are outputs
module name

## Slide 6: Module Instantiation
You can instantiate your own modules or pre-defined gates
  Always inside another module
Predefined: and, nand, or, nor, xor, xnor
  For these gates, port order is (output, input(s))
For your modules, port order is however you defined it
module mymodule(a, b, c, f);
output f;
input a, b, c;
module_name inst_name(port_connections);
endmodule
name of module to instantiate
name of instance
connect the ports

## Slide 7: Connecting Ports (By Order or Name)
In module instantiation, can specify port connections by name or by order
Use by-name connections (where possible)
module mod1(input a, b, output f);
// ...
endmodule
// by order
module mod2(input c, d, output g);
mod1 i0(c, d, g);
endmodule
// by name
module mod3(input c, d, output g);
mod1 i0(.f(g), .b(d), .a(c));
endmodule

## Slide 8: Structural Design
Example: multiplexor
  Output equals an input
  Which one depends on “sel”
module mux(a, b, sel, f);
output f;
input a, b, sel;
logic c, d, not_sel;
not gate0(not_sel, sel);
and gate1(c, a, not_sel);
and gate2(d, b, sel);
or gate3(f, c, d);
endmodule
datatype for describing logical value
Built-in gates:
port order is:
output, input(s)

## Slide 9: Continuous Assignment
Specify logic behaviorally by writing an expression to show how the signals are related to each other.
  assign statement
module mux2(a, b, sel, f);
output f;
input a, b, sel;
logic c, d;
assign c = a & (~sel);
assign d = b & sel;
assign f = c | d;
// or alternatively
assign f = sel ? b : a;
endmodule
c
d

## Slide 10: Combinational Procedural Block
Can use always_comb procedural block to describe combinational logic using a series of sequential statements
module mymodule(a, b, c, f);
output f;
input a, b, c;
always_comb begin
// Combinational logic
// described
// in C-like syntax
end
endmodule
All always_comb blocks are independent and parallel to each other

## Slide 11: Procedural Mux Description
module mux3(a, b, sel, f);
output logic f;
input a, b, sel;
always_comb begin
if (sel == 0) begin
f = a;
end
else begin
f = b;
end
end
endmodule
Important: for behavior to be combinational, every output (f) must be assigned in all possible control paths
Why? Otherwise, would be a latch and not combinational logic.
If we are going to drive f this way, need to declare it as logic

## Slide 12: Accidental Latch Description
This is not combinational, because for certain values of b, f must remember its previous value.
This code describes a latch. (If you want a latch, you should define it using always_latch)
module bad(a, b, f);
output logic f;
input a, b;
always_comb begin
if (b == 1) begin
f = a;
end
end
endmodule

## Slide 13: Multiply-Assigned Values
Both of these blocks execute concurrently
So what is the value of b? We don’t know!
module bad2(...);
...
always_comb begin
b = ... something ...
end
always_comb begin
b = ... something else ...
end
endmodule
Don’t do this!

## Slide 14: Multi-Bit Values
Can define inputs, outputs, or logic with multiple bits
module mux4(a, b, sel, f);
output logic [3:0] f;
input [3:0] a, b;
input sel;
always_comb begin
if (sel == 0) begin
f = a;
end
else begin
f = b;
end
end
endmodule

## Slide 15: Multi-Bit Constants and Concat
Can give constants with specified number bits
  In binary or hexadecimal
Can concatenate with { and }
Can reverse order (to index buffers left-to-right)
logic [3:0] a, b, c;
logic signed [3:0] d;
logic [7:0] e;
logic [1:0] f;
assign a = 4’b0010; // four bits, specified in binary
assign b = 4’hC; // four bits, specified in hex == 1100
assign c = 3; // == 0011
assign d = -2; // 2’s complement == 1110 as bits
assign e = {a, b}; // concatenate == 0010_1100
assign f = a[2 : 1]; // two bits from middle == 01

## Slide 16: Case Statements and “Don’t-Cares”
module newmod(out, in0, in1, in2);
input in0, in1, in2;
output logic out;
always_comb begin
case({in0, in1, in2})
3'b000: out = 1;
3'b001: out = 0;
3'b010: out = 0;
3'b011: out = x;
3'b10x: out = 1;
default: out = 0;
endcase
end
endmodule
output value is undefined in this case
last bit is a “don’t care” -- this line will be active for 100 OR 101
default gives “else” behavior. Here active if 110 or 111

## Slide 17: Arithmetic Operators
Standard arithmetic operators defined: + - * / %
Many subtleties here, so be careful:
  four bit number + four bit number = five bit number
    Or just the bottom four bits
  arbitrary division is difficult

## Slide 18: Addition and Subtraction
Be wary of overflow!
Use “signed” if you want, values as 2’s complement
logic [3:0] a, b;
logic [4:0] c;
assign c = a + b;
logic [3:0] d, e, f;
assign f = d + e;
4’b1000 + 4’b1000 = …
Overflows to zero
Five bit output can prevent overflow:
4’b1000 + 4’b1000 gives 5’b10000
logic signed [3:0] g, h, i;
logic signed [4:0] j;
assign g = 4’b0001; // == 1
assign h = 4’b0111; // == 7
assign i = g – h;
assign j = g – h;
i == 4’b1010 == -6
j == 5’b11010 == -6

## Slide 19: Multiplication
Multiply k bit number with m bit number
  How many bits does the result have?
If you use fewer bits in your code
  Gets least significant bits of the product
k+m
logic signed [3:0] a, b;
logic signed [7:0] c;
assign a = 4'b1110; // -2
assign b = 4'b0111; // 7
assign c = a*b;
c = 8’b1111_0010 == -14
logic signed [3:0] a, b, d;
assign a = 4'b1110; // -2
assign b = 4'b0111; // 7
assign d = a*b;
d = 4’0010 == 2
Underflow!

## Slide 20: Sequential Design
Everything so far was purely combinational
  stateless
What about sequential systems?
  flip-flops, registers, finite state machines
New constructs
  always_ff @(posedge clk, …)
  non-blocking assignment <=

## Slide 21: Edge-Triggered Events
Variant of always block called always_ff
  Indicates that block will be sequential logic (flip flops)
Procedural block occurs only on a signal’s edge
  @(posedge …) or @(negedge …)
always_ff @(posedge clk, negedge reset_n) begin
// This procedure will be executed
// anytime clk goes from 0 to 1
// or anytime reset_n goes from 1 to 0
end

## Slide 22: Flip Flops (1/3)
q remembers what d was at the last clock edge
  One bit of memory
Without reset:
module flipflop(d, q, clk);
input d, clk;
output logic q;
always_ff @(posedge clk) begin
q <= d;
end
endmodule

## Slide 23: Flip Flops (2/3)
Asynchronous reset:
module flipflop_asyncr(d, q, clk, rst_n);
input d, clk, rst_n;
output logic q;
always_ff @(posedge clk, negedge rst_n) begin
if (rst_n == 0)
q <= 0;
else
q <= d;
end
endmodule

## Slide 24: Flip Flops (3/3)
Synchronous reset:
module flipflop_syncr(d, q, clk, rst_n);
input d, clk, rst_n;
output logic q;
always_ff @(posedge clk) begin
if (rst_n == 0)
q <= 0;
else
q <= d;
end
endmodule

## Slide 25: Multi-Bit Flip Flop
module flipflop_asyncr(d, q, clk, rst_n);
input [15:0] d;
input clk, rst_n;
output logic [15:0] q;
always_ff @(posedge clk, negedge rst_n) begin
if (rst_n == 0)
q <= 0;
else
q <= d;
end
endmodule

## Slide 26: Digression: Module Parameters
Parameters allow modules to be easily changed
Instantiate and set parameter:
module my_flipflop(d, q, clk, rst_n);
parameter WIDTH=16;
input [WIDTH-1:0] d;
input clk, rst_n;
output logic [WIDTH-1:0] q;
...
endmodule
my_flipflop #(12) f0(d, q, clk, rst_n);
my_flipflop f0(d, q, clk, rst_n);
default value set to 16
uses default value
changes parameter to 12 for this instance
my_flipflop #(.WIDTH(12)) f0(d, q, clk, rst_n);

## Slide 27: Non-Blocking Assignment a <= b;
<= is the non-blocking assignment operator
  All left-hand side values take new values concurrently
This models synchronous logic!
always_ff @(posedge clk) begin
b <= a;
c <= b;
end
c gets the old value of b, not value assigned just above

## Slide 28: Non-Blocking vs. Blocking
Use non-blocking assignment <= to describe edge-triggered (synchronous) assignments
Use blocking assignment = to describe combinational assignment
always_ff @(posedge clk) begin
b <= a;
c <= b;
end
always_comb begin
b = a;
c = b;
end

## Slide 29: Finite State Machines (1/2)
State names
Output values
Transition values
Reset state

## Slide 30: Finite State Machines (2/2)
What does an FSM look like when implemented?
Combinational logic and registers
  Things we already know how to do!

## Slide 31: Full FSM Example (1/2)
module fsm(clk, rst, x, y);
input clk, rst, x;
output logic [1:0] y;
enum { STATEA=2'b00, STATEB=2'b01, STATEC=2'b10, STATED=2'b11 } state, next_state;
// next state logic
always_comb begin
case(state)
STATEA: next_state = x ? STATEB : STATEA;
STATEB: next_state = x ? STATEC : STATED;
STATEC: next_state = x ? STATED : STATEA;
STATED: next_state = x ? STATEC : STATEB;
endcase
end
// ... continued on next slide

## Slide 32: Full FSM Example (2/2)
// ... continued from previous slide
// register
always_ff @(posedge clk) begin
if (rst)
state <= STATEA;
else
state <= next_state;
end
// Output logic
always_comb begin
case(state)
STATEA: y = 2'b00;
STATEB: y = 2'b00;
STATEC: y = 2'b11;
STATED: y = 2'b10;
endcase
end
endmodule

## Slide 33: Arrays
module multidimarraytest();
logic [3:0] myarray [2:0];
assign myarray[0] = 4'b0010;
assign myarray[1][3:2] = 2'b01;
assign myarray[1][1] = 1'b1;
assign myarray[1][0] = 1'b0;
assign myarray[2][3:0] = 4'hC;
initial begin
$display("myarray == %b", myarray);
$display("myarray[2:0] == %b", myarray[2:0]);
$display("myarray[1:0] == %b", myarray[1:0];
$display("myarray[1] == %b", myarray[1]);
$display("myarray[1][2] == %b", myarray[1][2]);
$display("myarray[2][1:0] == %b", myarray[2][1:0]);
end
endmodule

## Slide 34: Memory (Combinational read)
module mymemory(clk, data_in, data_out, r_addr, w_addr, wr_en);
parameter WIDTH=16, LOGSIZE=8;
localparam SIZE=2**LOGSIZE;
input [WIDTH-1:0] data_in;
output logic [WIDTH-1:0] data_out;
input clk, wr_en;
input [LOGSIZE-1:0] r_addr, w_addr;
logic [WIDTH-1:0] mem [SIZE-1:0];
always_comb data_out = mem[r_addr];
end always_ff @(posedge clk) begin
if (wr_en)
mem[w_addr] <= data_in;
end
endmodule
Combinational read
Synchronous write

## Slide 35: Memory (Synchronous read)
module mymemory2(clk, data_in, data_out, r_addr, w_addr, wr_en);
parameter WIDTH=16, LOGSIZE=8;
localparam SIZE=2**LOGSIZE;
input [WIDTH-1:0] data_in;
output logic [WIDTH-1:0] data_out;
input clk, wr_en;
input [LOGSIZE-1:0] r_addr, w_addr;
logic [WIDTH-1:0] mem [SIZE-1:0];
always_ff @(posedge clk) begin
data_out <= mem[r_addr];
if (wr_en)
mem[w_addr] <= data_in;
end
endmodule
Synchronous read
What happens if we try to read and write the same address?

## Slide 36: Assertions
Assertions are test constructs
  Automatically validated as design is simulated
  Written for properties that must always be true
Makes it easier to test designs
  Don’t have to manually check for these conditions

## Slide 37: Example: A Good Place for Assertions
Imagine you have a FIFO queue
  When queue is full, it sets status_full to true
  When queue is empty, it sets status_empty to true
When status_full is true, wr_en must be false
When status_empty is true, rd_en must be false

## Slide 38: Assertions
Checks an expression when statement is executed
SV also has Concurrent Assertions
  Continuously monitored and can express temporal conditions
  Complex, but very powerful
    http://www.doulos.com/knowhow/sysverilog/tutorial/assertions/
// general form
assertion_name: assert(expression) pass_code;
else fail_code;
// example
always @(posedge clk) begin
assert((status_full == 0) || (wr_en == 0))
else $error("Tried to write to FIFO when full.");
end
Use $display to print text, $error to print error, or $fatal to print and halt simulation