## Slide 1: CSE 502: Computer Architecture
Out-of-Order Execution and Register Rename

## Slide 2: In Search of Parallelism
“Trivial” Parallelism is limited
  What is trivial parallelism?
    In-order: sequential instructions do not have dependencies
    In all previous cases, all insns. executed with or after earlier insns.
  Superscalar execution quickly hits a ceiling due to deps.
So what is “non-trivial” parallelism? …

## Slide 3: Instruction-Level Parallelism (ILP)
ILP is a measure of inter-dependencies between insns.
Average ILP = num. instruction / num. cyc required
code1: ILP = 1
  i.e. must execute serially
code2: ILP = 3
  i.e. can execute at the same time
code1: r1  r2 + 1
r3  r1 / 17
r4  r0 - r3
code2: r1  r2 + 1
r3  r9 / 17
r4  r0 - r10

## Slide 4: The Problem with In-Order Pipelines
What’s happening in cycle 4?
  mulf stalls due to RAW hazard
    OK, this is a fundamental problem
  subf stalls due to pipeline hazard
    Why? subf can’t proceed into D because mulf is there
    That is the only reason, and it isn’t a fundamental one
Why can’t subf go to D in cycle 4 and E+ in cycle 5?
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
addf f0,f1,f2 | F | D | E+ | E+ | E+ | W |  |  |  |  |  |  |  |  |  | 
mulf f2,f3,f2 |  | F | D | d* | d* | E* | E* | E* | E* | E* | W |  |  |  |  | 
subf f0,f1,f4 |  |  | F | p* | p* | D | E+ | E+ | E+ | W |  |  |  |  |  | 

## Slide 5: ILP != IPC
ILP usually assumes
  Infinite resources
  Perfect fetch
  Unit-latency for all instructions
ILP is a property of the program dataflow
IPC is the “real” observed metric
  How many insns. are executed per cycle
ILP is an upper-bound on the attainable IPC
  Specific to a particular program

## Slide 6: OoO Execution (1/3)
Dynamic scheduling
  Totally in the hardware
  Also called Out-of-Order execution (OoO)
Fetch many instructions into instruction window
  Use branch prediction to speculate past branches
Rename regs. to avoid false deps. (WAW and WAR)
Execute insns. as soon as possible
  As soon as deps. (regs and memory) are known
Today’s machines: 100+ insns. scheduling window

## Slide 7: Out-of-Order Execution (2/3)
Execute insns. in dataflow order
  Often similar but not the same as program order
Use register renaming removes false deps.
Scheduler identifies when to run insns.
  Wait for all deps. to be satisfied

## Slide 8: Out-of-Order Execution (3/3)
Static
Program
Fetch
Dynamic
Instruction
Stream
Rename
Renamed
Instruction
Stream
Schedule
Dynamically
Scheduled
Instructions
Out-of-order =
out of the original
sequential order
Notes: Just a pictoral view of the different steps

## Slide 9: Superscalar != Out-of-Order
A: R1 = Load 16[R2]
B: R3 = R1 + R4
C: R6 = Load 8[R9]
D: R5 = R2 – 4
E: R7 = Load 20[R5]
F: R4 = R4 – 1
G: BEQ R4, #0
C
D
E
cache miss
B
C
D
E
F
G
10 cycles
B
F
G
7 cycles
A
B
C
D
E
F
G
C
D
F
E
G
B
5 cycles
B
C
D
E
F
G
8 cycles
A
cache miss
1-wide
In-Order
A
cache miss
2-wide
In-Order
A
1-wide
Out-of-Order
A
cache miss
2-wide
Out-of-Order
Notes: Superscalar/In-order is not uncommon; Out-of-order/Single-Issue is not common (but possible).

## Slide 10: Example Pipeline Terminology
In-order pipeline
  F: Fetch
  D: Decode
  X: Execute
  W: Writeback
regfile
D$
I$
BP

## Slide 11: Example Pipeline Diagram
Alternative pipeline diagram
  Down: insns
  Across: pipeline stages
  In boxes: cycles
  Basically: stages  cycles
  Convenient for out-of-order
Insn | D | X | W
ldf X(r1),f1 | c1 | c2 | c3
mulf f0,f1,f2 | c3 | c4+ | c7
stf f2,Z(r1) | c7 | c8 | c9
addi r1,4,r1 | c8 | c9 | c10
ldf X(r1),f1 | c10 | c11 | c12
mulf f0,f1,f2 | c12 | c13+ | c16
stf f2,Z(r1) | c16 | c17 | c18

## Slide 12: Instruction Buffer
Trick: instruction buffer (a.k.a. instruction window)
  A bunch of registers for holding insns.
Split D into two parts
  Accumulate decoded insns. in buffer in-order
  Buffer sends insns. down rest of pipeline out-of-order
regfile
D$
insn buffer
I$
BP

## Slide 13: Dispatch and Issue
Dispatch (D): first part of decode
  Allocate slot in insn. buffer (if buffer is not full)
  In order: blocks younger insns.
Issue (S): second part of decode
  Send insns. from insn. buffer to execution units
  Out-of-order: doesn’t block younger insns.
regfile
D$
insn buffer
I$
BP

## Slide 14: Dispatch and Issue with Floating-Point
regfile
D$
I$
BP
F-regfile
E/
E
+
E
+
E*
E*
E*
insn buffer
  Number of pipeline stages per FU can vary

## Slide 15: Our-of-Order Topics
“Scoreboarding”
  First OoO, no register renaming
“Tomasulo’s algorithm”
  OoO with register renaming
Handling precise state and speculation
  P6-style execution (Intel Pentium Pro)
  R10k-style execution (MIPS R10k)
Handling memory dependencies

## Slide 16: In-Order Issue, OoO Completion
Issue stage needs to check:
1. Structural Dependence
2. RAW Hazard
3. WAW Hazard
4. WAR Hazard
Issue = send an instruction
to execution
INT
Fadd1
Fadd2
Fmul1
Fmul2
Fmul3
Ld/St
In-order
Inst.
Stream
Execution
Begins
In-order
Out-of-order
Completion

## Slide 17: Track with Simple Scoreboarding
Scoreboard: a bit-array, 1-bit for each GPR
  If the bit is not set: the register has valid data
  If the bit is set: the register has stale data
    i.e., some outstanding instruction is going to change it
Issue in Order: RD  Fn (RS, RT)
  If SB[RS] or SB[RT] is set  RAW, stall
  If SB[RD] is set  WAW, stall
  Else, dispatch to FU (Fn) and set SB[RD]
Complete out-of-order
  Update GPR[RD], clear SB[RD]
Notes: H&P-style notation

## Slide 18: Review of Register Dependencies
A: R1 = R2 + R3
B: R4 = R1 * R4
5
-2
9
3
R1
R2
R3
R4
Read-After-Write
7
-2
9
3
7
-2
9
21
A
B
5
-2
9
3
R1
R2
R3
R4
5
-2
9
15
7
-2
9
15
B
A
A: R1 = R3 / R4
B: R3 = R2 * R4
Write-After-Read
5
-2
9
3
R1
R2
R3
R4
3
-2
9
3
3
-2
-6
3
A
B
5
-2
9
3
R1
R2
R3
R4
5
-2
-6
3
-2
-2
-6
3
A
B
Write-After-Write
A: R1 = R2 + R3
B: R1 = R3 * R4
5
-2
9
3
R1
R2
R3
R4
7
-2
9
3
27
-2
9
3
A
B
5
-2
9
3
R1
R2
R3
R4
27
-2
9
3
7
-2
9
3
A
B
Notes: This should be review. Each is an example of how you will get the wrong results if you reorder two instructions that have a register dependency.

## Slide 19: Eliminating WAR Dependencies
WAR dependencies are from reusing registers
A: R1 = R3 / R4
B: R3 = R2 * R4
5
-2
9
3
R1
R2
R3
R4
3
-2
9
3
3
-2
-6
3
A
B
5
-2
9
3
R1
R2
R3
R4
5
-2
-6
3
-2
-2
-6
3
B
A
5
-2
9
3
R1
R2
R3
R4
5
-2
9
3
3
-2
9
3
B
A
4
R5
-6
-6
A: R1 = R3 / R4
B: R5 = R2 * R4
X
  Can get correct result just by using different reg.
Notes: example shows how using a different architected register removes WAR

## Slide 20: Eliminating WAW Dependencies
WAW dependencies are also from reusing registers
5
-2
9
3
R1
R2
R3
R4
27
-2
9
3
27
-2
9
3
B
A
4
R5
4
7
A: R1 = R2 + R3
B: R1 = R3 * R4
5
-2
9
3
R1
R2
R3
R4
7
-2
9
3
27
-2
9
3
A
B
5
-2
9
3
R1
R2
R3
R4
27
-2
9
3
7
-2
9
3
A
B
A: R5 = R2 + R3
B: R1 = R3 * R4
X
  Can get correct result just by using different reg.
Notes: example shows similar for WAW

## Slide 21: Register Renaming
Register renaming (in hardware)
  “Change” register names to eliminate WAR/WAW hazards
  Arch. registers (r1,f0…) are names, not storage locations
  Can have more locations than names
  Can have multiple active versions of same name
How does it work?
  Map-table: maps names to most recent locations
  On a write: allocate new location, note in map-table
  On a read: find location of most recent write via map-table

## Slide 22: Register Renaming
Anti (WAR) and output (WAW) deps. are false
  Dep. is on name/location, not on data
  Given infinite registers, WAR/WAW don’t arise
  Renaming removes WAR/WAW, but leaves RAW intact
Example
  Names: r1,r2,r3 Locations: p1,p2,p3,p4,p5,p6,p7
  Original: r1p1, r2p2, r3p3, p4–p7 are “free”
MapTable |  |  |  | FreeList |  | Original insns. |  | Renamed insns.
r1 | r2 | r3 |  |  |  |  |  | 
p1 | p2 | p3 |  | p4,p5,p6,p7 |  | add r2,r3,r1 |  | add p2,p3,p4
p4 | p2 | p3 |  | p5,p6,p7 |  | sub r2,r1,r3 |  | sub p2,p4,p5
p4 | p2 | p5 |  | p6,p7 |  | mul r2,r3,r3 |  | mul p2,p5,p6
p4 | p2 | p6 |  | p7 |  | div r1,4,r1 |  | div p4,4,p7

## Slide 23: Register Renaming
Anti (WAR) and output (WAW) deps. are false
  Dep. is on name/location, not on data
  Given infinite registers, WAR/WAW don’t arise
  Renaming removes WAR/WAW, but leaves RAW intact
Example
  Names: r1,r2,r3 Locations: p1,p2,p3,p4,p5,p6,p7
  Original: r1p1, r2p2, r3p3, p4–p7 are “free”
MapTable |  |  |  | FreeList |  | Original insns. |  | Renamed insns.
r1 | r2 | r3 |  |  |  |  |  | 
p1 | p2 | p3 |  | p4,p5,p6,p7 |  | add r2,r3,r1 |  | add p2,p3,p4
p4 | p2 | p3 |  | p5,p6,p7 |  | sub r2,r1,r3 |  | sub p2,p4,p5
p4 | p2 | p5 |  | p6,p7 |  | mul r2,r3,r3 |  | mul p2,p5,p6
p4 | p2 | p6 |  | p7 |  | div r1,4,r1 |  | div p4,4,p7

## Slide 24: Tomasulo’s Algorithm
Reservation Stations (RS): instruction buffer
Common data bus (CDB): broadcasts results to RS
Register renaming: removes WAR/WAW hazards
Bypassing (not shown here to make example simpler)

## Slide 25: Tomasulo Data Structures (1/2)
Reservation Stations (RS)
  FU, busy, op, R: destination register name
  T: destination register tag (RS# of this RS)
  T1,T2: source register tag (RS# of RS that will output value)
  V1,V2: source register values
Map Table (a.k.a., RAT)
  T: tag (RS#) that will write this register
Common Data Bus (CDB)
  Broadcasts <RS#, value> of completed insns.
Valid tags indicate the RS# that will produce result
  T==0  Value is ready somewhere
  T!=0  Value is not ready, wait until CDB broadcasts T

## Slide 26: Tomasulo Data Structures (2/2)
value
V1
V2
FU
T
T2
T1
T
op
==
==
==
==
Map Table
Reservation Stations
CDB.V
CDB.T
Fetched
insns
Regfile
R
T
==
==
==
==

## Slide 27: Tomasulo Pipeline
New pipeline structure: F, D, S, X, W
  D (dispatch)
    Structural hazard ? stall : allocate RS entry
  S (issue)
    RAW hazard ? wait (monitor CDB) : go to execute
  W (writeback)
    Write register, free RS entry
    W and RAW-dependent S in same cycle
    W and structural-dependent D in same cycle

## Slide 28: Tomasulo Dispatch (D)
Allocate RS entry (structural stall if busy)
  Input register ready ? read value into RS : read tag into RS
  Set register status (i.e., rename) for output register
value
V1
V2
FU
T
T2
T1
T
op
==
==
==
==
Map Table
Reservation Stations
CDB.V
CDB.T
Fetched
insns
Regfile
R
T
==
==
==
==

## Slide 29: Tomasulo Issue (S)
Wait for RAW hazards
  Read register values from RS
value
V1
V2
FU
T
T2
T1
T
op
==
==
==
==
Map Table
Reservation Stations
CDB.V
CDB.T
Fetched
insns
Regfile
R
T
==
==
==
==

## Slide 30: Tomasulo Execute (X)
value
V1
V2
FU
T
T2
T1
T
op
==
==
==
==
Map Table
Reservation Stations
CDB.V
CDB.T
Fetched
insns
Regfile
R
T
==
==
==
==

## Slide 31: Tomasulo Writeback (W)
Wait for structural (CDB) hazards
  Output Reg tag still matches? clear, write result to register
  CDB broadcast to RS: tag match ? clear tag, copy value
value
V1
V2
FU
T
T2
T1
T
op
==
==
==
==
Map Table
Reservation Stations
CDB.V
CDB.T
Fetched
insns
Regfile
R
T
==
==
==
==

## Slide 32: Where is the “register rename”?
Value copies in RS (V1, V2)
Insn. stores correct input values in its own RS entry
“Free list” is implicit (allocate/deallocate as part of RS)
value
V1
V2
FU
T
T2
T1
T
op
==
==
==
==
Map Table
Reservation Stations
CDB.V
CDB.T
Fetched
insns
Regfile
R
T
==
==
==
==

## Slide 33: Tomasulo Data Structures
Insn Status |  |  |  | 
Insn | D | S | X | W
ldf X(r1),f1 |  |  |  | 
mulf f0,f1,f2 |  |  |  | 
stf f2,Z(r1) |  |  |  | 
addi r1,4,r1 |  |  |  | 
ldf X(r1),f1 |  |  |  | 
mulf f0,f1,f2 |  |  |  | 
stf f2,Z(r1) |  |  |  | 
Map Table | 
Reg | T
f0 | 
f1 | 
f2 | 
r1 | 
Reservation Stations |  |  |  |  |  |  |  | 
T | FU | busy | op | R | T1 | T2 | V1 | V2
1 | ALU | no |  |  |  |  |  | 
2 | LD | no |  |  |  |  |  | 
3 | ST | no |  |  |  |  |  | 
4 | FP1 | no |  |  |  |  |  | 
5 | FP2 | no |  |  |  |  |  | 
CDB | 
T | V

## Slide 34: Tomasulo: Cycle 1
Insn Status |  |  |  | 
Insn | D | S | X | W
ldf X(r1),f1 | c1 |  |  | 
mulf f0,f1,f2 |  |  |  | 
stf f2,Z(r1) |  |  |  | 
addi r1,4,r1 |  |  |  | 
ldf X(r1),f1 |  |  |  | 
mulf f0,f1,f2 |  |  |  | 
stf f2,Z(r1) |  |  |  | 
Map Table | 
Reg | T
f0 | 
f1 | RS#2
f2 | 
r1 | 
Reservation Stations |  |  |  |  |  |  |  | 
T | FU | busy | op | R | T1 | T2 | V1 | V2
1 | ALU | no |  |  |  |  |  | 
2 | LD | yes | ldf | f1 | - | - | - | [r1]
3 | ST | no |  |  |  |  |  | 
4 | FP1 | no |  |  |  |  |  | 
5 | FP2 | no |  |  |  |  |  | 
CDB | 
T | V
allocate

## Slide 35: Tomasulo: Cycle 2
Insn Status |  |  |  | 
Insn | D | S | X | W
ldf X(r1),f1 | c1 | c2 |  | 
mulf f0,f1,f2 | c2 |  |  | 
stf f2,Z(r1) |  |  |  | 
addi r1,4,r1 |  |  |  | 
ldf X(r1),f1 |  |  |  | 
mulf f0,f1,f2 |  |  |  | 
stf f2,Z(r1) |  |  |  | 
Map Table | 
Reg | T
f0 | 
f1 | RS#2
f2 | RS#4
r1 | 
Reservation Stations |  |  |  |  |  |  |  | 
T | FU | busy | op | R | T1 | T2 | V1 | V2
1 | ALU | no |  |  |  |  |  | 
2 | LD | yes | ldf | f1 | - | - | - | [r1]
3 | ST | no |  |  |  |  |  | 
4 | FP1 | yes | mulf | f2 | - | RS#2 | [f0] | -
5 | FP2 | no |  |  |  |  |  | 
CDB | 
T | V
allocate

## Slide 36: Tomasulo: Cycle 3
Insn Status |  |  |  | 
Insn | D | S | X | W
ldf X(r1),f1 | c1 | c2 | c3 | 
mulf f0,f1,f2 | c2 |  |  | 
stf f2,Z(r1) | c3 |  |  | 
addi r1,4,r1 |  |  |  | 
ldf X(r1),f1 |  |  |  | 
mulf f0,f1,f2 |  |  |  | 
stf f2,Z(r1) |  |  |  | 
Map Table | 
Reg | T
f0 | 
f1 | RS#2
f2 | RS#4
r1 | 
Reservation Stations |  |  |  |  |  |  |  | 
T | FU | busy | op | R | T1 | T2 | V1 | V2
1 | ALU | no |  |  |  |  |  | 
2 | LD | yes | ldf | f1 | - | - | - | [r1]
3 | ST | yes | stf | - | RS#4 | - | - | [r1]
4 | FP1 | yes | mulf | f2 | - | RS#2 | [f0] | -
5 | FP2 | no |  |  |  |  |  | 
CDB | 
T | V
allocate

## Slide 37: Tomasulo: Cycle 4
Insn Status |  |  |  | 
Insn | D | S | X | W
ldf X(r1),f1 | c1 | c2 | c3 | c4
mulf f0,f1,f2 | c2 | c4 |  | 
stf f2,Z(r1) | c3 |  |  | 
addi r1,4,r1 | c4 |  |  | 
ldf X(r1),f1 |  |  |  | 
mulf f0,f1,f2 |  |  |  | 
stf f2,Z(r1) |  |  |  | 
Map Table | 
Reg | T
f0 | 
f1 | RS#2
f2 | RS#4
r1 | RS#1
Reservation Stations |  |  |  |  |  |  |  | 
T | FU | busy | op | R | T1 | T2 | V1 | V2
1 | ALU | yes | addi | r1 | - | - | [r1] | -
2 | LD | no |  |  |  |  |  | 
3 | ST | yes | stf | - | RS#4 | - | - | [r1]
4 | FP1 | yes | mulf | f2 | - | RS#2 | [f0] | CDB.V
5 | FP2 | no |  |  |  |  |  | 
CDB | 
T | V
RS#2 | [f1]
allocate
ldf finished (W)
clear f1 RegStatus
CDB broadcast
free
RS#2 ready 
grab CDB value

## Slide 38: Tomasulo: Cycle 5
Insn Status |  |  |  | 
Insn | D | S | X | W
ldf X(r1),f1 | c1 | c2 | c3 | c4
mulf f0,f1,f2 | c2 | c4 | c5 | 
stf f2,Z(r1) | c3 |  |  | 
addi r1,4,r1 | c4 | c5 |  | 
ldf X(r1),f1 | c5 |  |  | 
mulf f0,f1,f2 |  |  |  | 
stf f2,Z(r1) |  |  |  | 
Map Table | 
Reg | T
f0 | 
f1 | RS#2
f2 | RS#4
r1 | RS#1
Reservation Stations |  |  |  |  |  |  |  | 
T | FU | busy | op | R | T1 | T2 | V1 | V2
1 | ALU | yes | addi | r1 | - | - | [r1] | -
2 | LD | yes | ldf | f1 | - | RS#1 | - | -
3 | ST | yes | stf | - | RS#4 | - | - | [r1]
4 | FP1 | yes | mulf | f2 | - | - | [f0] | [f1]
5 | FP2 | no |  |  |  |  |  | 
CDB | 
T | V
allocate

## Slide 39: Tomasulo: Cycle 6
Insn Status |  |  |  | 
Insn | D | S | X | W
ldf X(r1),f1 | c1 | c2 | c3 | c4
mulf f0,f1,f2 | c2 | c4 | c5+ | 
stf f2,Z(r1) | c3 |  |  | 
addi r1,4,r1 | c4 | c5 | c6 | 
ldf X(r1),f1 | c5 |  |  | 
mulf f0,f1,f2 | c6 |  |  | 
stf f2,Z(r1) |  |  |  | 
Map Table | 
Reg | T
f0 | 
f1 | RS#2
f2 | RS#4RS#5
r1 | RS#1
Reservation Stations |  |  |  |  |  |  |  | 
T | FU | busy | op | R | T1 | T2 | V1 | V2
1 | ALU | yes | addi | r1 | - | - | [r1] | -
2 | LD | yes | ldf | f1 | - | RS#1 | - | -
3 | ST | yes | stf | - | RS#4 | - | - | [r1]
4 | FP1 | yes | mulf | f2 | - | - | [f0] | [f1]
5 | FP2 | yes | mulf | f2 | - | RS#2 | [f0] | -
CDB | 
T | V
allocate
no stall on WAW: scoreboard
overwrites f2 RegStatus
anyone who needs old f2 tag has it

## Slide 40: Tomasulo: Cycle 7
Insn Status |  |  |  | 
Insn | D | S | X | W
ldf X(r1),f1 | c1 | c2 | c3 | c4
mulf f0,f1,f2 | c2 | c4 | c5+ | 
stf f2,Z(r1) | c3 |  |  | 
addi r1,4,r1 | c4 | c5 | c6 | c7
ldf X(r1),f1 | c5 | c7 |  | 
mulf f0,f1,f2 | c6 |  |  | 
stf f2,Z(r1) |  |  |  | 
Map Table | 
Reg | T
f0 | 
f1 | RS#2
f2 | RS#5
r1 | RS#1
Reservation Stations |  |  |  |  |  |  |  | 
T | FU | busy | op | R | T1 | T2 | V1 | V2
1 | ALU | no |  |  |  |  |  | 
2 | LD | yes | ldf | f1 | - | RS#1 | - | CDB.V
3 | ST | yes | stf | - | RS#4 | - | - | [r1]
4 | FP1 | yes | mulf | f2 | - | - | [f0] | [f1]
5 | FP2 | yes | mulf | f2 | - | RS#2 | [f0] | -
CDB | 
T | V
RS#1 | [r1]
addi finished (W)
clear r1 RegStatus
CDB broadcast
RS#1 ready 
grab CDB value
no W wait on WAR: map table ensured
anyone who needs old r1 has RS copy
D stall on store RS: structural (no space)

## Slide 41: Tomasulo: Cycle 8
Insn Status |  |  |  | 
Insn | D | S | X | W
ldf X(r1),f1 | c1 | c2 | c3 | c4
mulf f0,f1,f2 | c2 | c4 | c5+ | c8
stf f2,Z(r1) | c3 | c8 |  | 
addi r1,4,r1 | c4 | c5 | c6 | c7
ldf X(r1),f1 | c5 | c7 | c8 | 
mulf f0,f1,f2 | c6 |  |  | 
stf f2,Z(r1) |  |  |  | 
Map Table | 
Reg | T
f0 | 
f1 | RS#2
f2 | RS#5
r1 | 
Reservation Stations |  |  |  |  |  |  |  | 
T | FU | busy | op | R | T1 | T2 | V1 | V2
1 | ALU | no |  |  |  |  |  | 
2 | LD | yes | ldf | f1 | - | - | - | [r1]
3 | ST | yes | stf | - | RS#4 | - | CDB.V | [r1]
4 | FP1 | no |  |  |  |  |  | 
5 | FP2 | yes | mulf | f2 | - | RS#2 | [f0] | -
CDB | 
T | V
RS#4 | [f2]
mulf finished (W), f2 already
overwritten by 2nd mulf (RS#5)
CDB broadcast
RS#4 ready 
grab CDB value

## Slide 42: Tomasulo: Cycle 9
Insn Status |  |  |  | 
Insn | D | S | X | W
ldf X(r1),f1 | c1 | c2 | c3 | c4
mulf f0,f1,f2 | c2 | c4 | c5+ | c8
stf f2,Z(r1) | c3 | c8 | c9 | 
addi r1,4,r1 | c4 | c5 | c6 | c7
ldf X(r1),f1 | c5 | c7 | c8 | c9
mulf f0,f1,f2 | c6 | c9 |  | 
stf f2,Z(r1) |  |  |  | 
Map Table | 
Reg | T
f0 | 
f1 | RS#2
f2 | RS#5
r1 | 
Reservation Stations |  |  |  |  |  |  |  | 
T | FU | busy | op | R | T1 | T2 | V1 | V2
1 | ALU | no |  |  |  |  |  | 
2 | LD | no |  |  |  |  |  | 
3 | ST | yes | stf | - | - | - | [f2] | [r1]
4 | FP1 | no |  |  |  |  |  | 
5 | FP2 | yes | mulf | f2 | - | RS#2 | [f0] | CDB.V
CDB | 
T | V
RS#2 | [f1]
RS#2 ready 
grab CDB value
2nd ldf finished (W)
clear f1 RegStatus
CDB broadcast

## Slide 43: Tomasulo: Cycle 10
Insn Status |  |  |  | 
Insn | D | S | X | W
ldf X(r1),f1 | c1 | c2 | c3 | c4
mulf f0,f1,f2 | c2 | c4 | c5+ | c8
stf f2,Z(r1) | c3 | c8 | c9 | c10
addi r1,4,r1 | c4 | c5 | c6 | c7
ldf X(r1),f1 | c5 | c7 | c8 | c9
mulf f0,f1,f2 | c6 | c9 | c10 | 
stf f2,Z(r1) | c10 |  |  | 
Map Table | 
Reg | T
f0 | 
f1 | 
f2 | RS#5
r1 | 
Reservation Stations |  |  |  |  |  |  |  | 
T | FU | busy | op | R | T1 | T2 | V1 | V2
1 | ALU | no |  |  |  |  |  | 
2 | LD | no |  |  |  |  |  | 
3 | ST | yes | stf | - | RS#5 | - | - | [r1]
4 | FP1 | no |  |  |  |  |  | 
5 | FP2 | yes | mulf | f2 | - | - | [f0] | [f1]
CDB | 
T | V
free  allocate
stf finished (W)
no output register  no CDB broadcast

## Slide 44: Can We Add Superscalar?
Dynamic scheduling and multi-issue are orthogonal
  N: superscalar width (number of parallel operations)
  W: window size (number of reservation stations)
What is needed for an N-by-W Tomasulo?
  RS: N tag/value write (D), N value read (S), 2N tag cmp (W)
  Select logic: WN priority encoder (S)
  MT: 2N read (D), N write (D)
  RF: 2N read (D), N write (W)
  CDB: N (W)