## Slide 1: CSE 502: Computer Architecture
Out-of-Order Schedulers

## Slide 2: Data-Capture Scheduler
Dispatch: read available operands from ARF/ROB, store in scheduler
Commit: Missing operands filled in from bypass
Issue: When ready, operands sent directly from scheduler to functional units
Fetch &
Dispatch
ARF
PRF/ROB
Data-Capture
Scheduler
Functional
Units
Physical register update
Bypass
Notes: P-Pro family processors use data-capture-style schedulers. Dispatch is usually the same as the Allocate (or just “alloc”) stage(s).

## Slide 3: Components of a Scheduler
A
B
C
D
F
E
G
Buffer for unexecuted
instructions
Method for tracking
state of dependencies
(resolved or not)
Arbiter
B
Method for choosing between multiple ready instructions competing for the same resource
Method for notification
of dependency resolution
“Scheduler Entries” or
“Issue Queue” (IQ) or
“Reservation Stations” (RS)
Notes: The scheduler is sometimes also called the “Instruction Window”, but that can be a little confusing as sometime the instruction window refers to all instructions in flight in the processor, which can include those that have issues/executed and left the IQ/RS.

## Slide 4: Scheduling Loop or Wakeup-Select Loop
Wake-Up Part:
  Executing instruction notifies dependents
  Waiting instructions check if all deps are satisfied
    If yes, “wake up” instruction
Select Part:
  Choose which instructions get to execute
    More than one insn. can be ready
    Number of functional units and memory ports are limited

## Slide 5: Scalar Scheduler (Issue Width = 1)
T14
T16
T39
T6
T17
T39
T15
T39
=
=
=
=
=
=
=
=
T39
T8
T17
T42
Select Logic
To Execute Logic
Tag Broadcast Bus
Notes: The boxes that turn green indicate the readiness of each of the operands.

## Slide 6: Superscalar Scheduler (detail of one entry)
Tags,
Ready
Logic
Select
Logic
Tag
Broadcast
Buses
=
=
=
=
=
=
=
=
bid
grants
SrcL
RdyL
ValL
Issued
SrcR
RdyR
ValR
Dst
Notes: Same logic as previous slide (but for one entry), but for four-way issue.

## Slide 7: Interaction with Execution
A
Select Logic
SR
D
SL
opcode
ValL
ValR
ValL
ValR
ValL
ValR
ValL
ValR
Payload RAM
Notes: D = Destination Tag, SL = Left Source Tag, SR = Right Source Tag, ValL = Left Operand Value, ValR = Right Operand Value
The scheduler is typically broken up into the CAM-based scheduling part, and a RAM-based “payload” part that holds the actual values (and instruction opcode and any other information required for execution) that get sent to the actual functional units/ALUs.

## Slide 8: Again, But Superscalar
A
B
Select Logic
SR
SR
D
D
SL
SL
opcode
ValL
ValR
ValL
ValR
ValL
ValR
ValL
ValR
opcode
ValL
ValR
ValL
ValR
ValL
ValR
  Scheduler captures values
Notes: D = Destination Tag, SL = Left Source Tag, SR = Right Source Tag, ValL = Left Operand Value, ValR = Right Operand Value
The animation shows the wakeup process on the left, and then illustrates how the same tag matches used in the wakeup can also be used to enable the capturing of output values on the data-path side.

## Slide 9: Issue Width
Max insns. selected each cycle is issue width
  Previous slides showed different issue widths
    four, one, and two
Hardware requirements:
  Naively, issue width of N requires N tag broadcast buses
  Can “specialize” some of the issue slots
    E.g., a slot that only executes branches (no outputs)

## Slide 10: Simple Scheduler Pipeline
Select
Payload
Wakeup
A:
Execute
Capture
B:
tag broadcast
result
broadcast
enable
capture
on tag match
Select
Payload
Execute
Wakeup
Capture
C:
enable
capture
tag broadcast
Cycle i
Cycle i+1
A
B
C
  Very long clock cycle
Notes: Simple case with minimal pipelining; dependent instructions can execute in back-to-back cycles, but the achievable clock speed will be slow because each cycle contains too much work (i.e., select, payload read, execute, bypass and capture).

## Slide 11: Deeper Scheduler Pipeline
Select
Payload
A:
Execute
Capture
B:
tag broadcast
result
broadcast
enable
capture
Select
Payload
Execute
Capture
C:
enable
capture
tag broadcast
Cycle i
Cycle i+1
Select
Payload
Execute
Cycle i+2
Cycle i+3
Wakeup
Wakeup
A
B
C
  Faster, but Capture & Payload on same cycle
Notes: Faster clock speed

## Slide 12: Even Deeper Scheduler Pipeline
Select
Payload
A:
Execute
Capture
B:
tag broadcast
result broadcast
and bypass
enable
capture
C:
Cycle i
Wakeup
Select
Wakeup
Payload
Execute
Select
Payload
Execute
Capture
Cycle i+1
Cycle i+2
Cycle i+3
Capture
Wakeup
tag match
on first
operand
tag match
on second
operand
(now C is ready)
No simultaneous read/write!
A
B
C
Cycle i+4
  Need second level of bypassing

## Slide 13: Very Deep Scheduler Pipeline
Select
Payload
A:
Execute
Capture
C:
Cycle i
Wakeup
i+1
i+2
i+3
Select
Payload
Execute
Wakeup
Capture
Select
Payload
Execute
i+4
i+5
D:
A
C
B
D
Wakeup
Capture
B:
Select
Select
Payload
Execute
A&B both
ready, only
A selected,
B bids again
AC and CD must
be bypassed,
BD OK without bypass
i+6
  Dependent instructions can’t execute back-to-back
Notes: Very aggressive pipelining, but now with a greater IPC penalty due to not being able to issue dependent instructions in back-to-back cycles. Good segue to the many research papers on aggressive and/or speculative pipelining of the scheduler (quite a few of these in ISCA/MICRO/HPCA the early 2000’s).

## Slide 14: Pipelineing Critical Loops
Wakeup-Select Loop hard to pipeline
  No back-to-back execute
  Worst-case IPC is ½
Usually not worst-case
  Last example had IPC
A
B
C
A
B
C
Regular
Scheduling
No Back-
to-Back
  Studies indicate 10-15% IPC penalty

## Slide 15: IPC vs. Frequency
10-15% IPC not bad if frequency can double
Frequency doesn’t double
  Latch/pipeline overhead
  Stage imbalance
1000ps
500ps
500ps
2.0 IPC, 1GHz
1.7 IPC, 2GHz
2 BIPS
3.4 BIPS
900ps
450ps
450ps
900ps
350
550
1.5GHz
Notes: Just pointing out that the ideal performance (double clock speed combined with 10-15% IPC hit) is not likely achievable due to many other issues.

## Slide 16: Non-Data-Capture Scheduler
Fetch &
Dispatch
ARF
PRF
Scheduler
Functional
Units
Physical register
update
Fetch &
Dispatch
Unified
PRF
Scheduler
Functional
Units
Physical register
update

## Slide 17: Pipeline Timing
Select
Payload
Wakeup
Execute
Select
Payload
Execute
Select
Payload
Read Operands from PRF
Wakeup
Execute
Select
Payload
Read Operands from PRF
Exec
S
X
E
X
X
S
X
E
“Skip” Cycle
Substantial increase in schedule-to-execute latency
Data-Capture
Non-Data-Capture
Notes: The idea of a “skip” cycle is just to abstract away any work that has to be done between schedule and execute. This could be payload RAM reading, picking up values from the bypass bus, reading values from the physical register file, or simple wire delay to get the data from the scheduler logic all the way over to the execution units.
This example assumes a two-cycle PRF read latency: You read out the register identifier (e.g., “P13”) from the payload RAM, and then that is used as an index into the PRF to read the actual data value.

## Slide 18: Handling Multi-Cycle Instructions
Sched
PayLd
Exec
Sched
PayLd
Exec
Add R1 = R2 + R3
Xor R4 = R1 ^ R5
Sched
PayLd
Exec
Add R4 = R1 + R5
WU
Sched
PayLd
Exec
Mul R1 = R2 × R3
Exec
Exec
  Instructions can’t execute too early
WU

## Slide 19: Delayed Tag Broadcast (1/3)
Must make sure broadcast bus available in future
Bypass and data-capture get more complex
Sched
PayLd
Exec
Add R4 = R1 + R5
Sched
PayLd
Exec
Mul R1 = R2 × R3
Exec
Exec
WU

## Slide 20: Delayed Tag Broadcast (2/3)
Sched
PayLd
Exec
Add R4 = R1 + R5
Sched
PayLd
Exec
Mul R1 = R2 × R3
Exec
Exec
Sched
PayLd
Exec
Sub R7 = R8 – #1
Sched
PayLd
Exec
Xor R9 = R9 ^ R6
Assume
issue width
equals 2
In this cycle, three instructions
need to broadcast their tags!
WU
Notes: Just illustrating that if you delay the tag broadcast, you will need some mechanism to ensure that sufficient broadcast buses are available when it finally comes time to do the broadcast.

## Slide 21: Delayed Tag Broadcast (3/3)
Possible solutions
  One select for issuing, another select for broadcast
    Messes up timing of data-capture
  Pre-reserve the bus
    Complicated select logic, track current + future cycles
  Hold the issue slot from initial launch until tag broadcast
sch
payl
exec
exec
exec
Issue width effectively reduced by one for three cycles
Notes: I’m not sure how this is actually implemented in current processors, but my best guess is option #2. The scheduler has to keep a couple of tables/scoreboards/data-structures for tracking resource availability, but it probably already has to do this anyway for the functional units, so it would just be some more scoreboards (for tag broadcast bus, for the bypass buses, etc.).

## Slide 22: Delayed Wakeup
Push the delay to the consumer
=
Tag Broadcast for
R1 = R2 × R3
R1
=
R4
R5 = R1 + R4
ready!
Tag arrives, but we wait
three cycles before
acknowledging it
Must know ancestor’s latency
Notes: This is just another possibility, but I don’t think anyone would actually do this… variable latency instructions would probably cause an immense head-ache.

## Slide 23: Non-Deterministic Latencies
Previous approaches assume all latencies are known
Real situations have unknown latency
  Load instructions
    Latency  {L1_lat, L2_lat, L3_lat, DRAM_lat}
    DRAM_lat is not a constant either, queuing delays
  Architecture specific cases
    PowerPC 603 has “early out” for multiplication
    Intel Core 2 has early out divider also
Makes delayed broadcast hard
Kills delayed wakeup

## Slide 24: The Wait-and-See Approach
Complexity only in the case of variable-latency ops
  Most insns. have known latency
Wait to learn if load hits or misses in the cache
Sched
PayLd
Exec
R2 = R1 + #4
Sched
PayLd
Exec
R1 = 16[$sp]
Exec
Exec
Cache hit known,
can broadcast tag
Load-to-Use latency
increases by 2 cycles
(3 cycle load appears as 5)
Scheduler
DL1 Tags
DL1
Data
May be able to
design cache s.t.
hit/miss known
before data
Exec
Exec
Exec
Sched
PayLd
Exec
Penalty reduced to 1 cycle

## Slide 25: Load-Hit Speculation
Caches work pretty well
  Hit rates are high (otherwise we wouldn’t use caches)
  Assume all loads hit in the cache
Sched
PayLd
Exec
R2 = R1 + #4
Sched
PayLd
Exec
R1 = 16[$sp]
Exec
Exec
Cache hit,
data forwarded
Broadcast delayed
by DL1 latency
  What to do on a cache miss?

## Slide 26: Load-Hit Mis-speculation
Sched
PayLd
Exec
Sched
PayLd
Exec
Exec
Exec
Broadcast delayed
by DL1 latency
Exec
…
Exec
Cache Miss Detected!
Value at cache output is bogus
Invalidate the instruction
(ALU output ignored)
Sched
PayLd
Exec
Rescheduled assuming
a hit at the DL2 cache
There could be a miss at the L2 and again at the L3 cache. A single load can waste multiple issuing opportunities.
Each mis-scheduling wastes an issue slot:
the tag broadcast bus, payload RAM read port, writeback/bypass bus, etc. could have been used for another instruction
Broadcast delayed by L2 latency
L2 hit
  It’s hard, but we want this for performance

## Slide 27: “But wait, there’s more!”
Sched
PayLd
Exec
Sched
PayLd
Exec
Exec
Exec
L1-D Miss
Sched
PayLd
Exec
Sched
PayLd
Exec
Sched
PayLd
Exec
Squash
Not only children get
squashed, there may be grand-children to squash as well
All waste issue slots
All must be rescheduled
All waste power
None may leave scheduler
until load hit known
Sched
PayLd
Exec
Sched
PayLd
Exec
Sched
PayLd
Exec
Sched
PayLd
Exec
Notes: The longer the schedule-to-execute latency, the more “generations” of dependent instructions could be speculatively mis-scheduled.

## Slide 28: Squashing (1/3)
Squash “in-flight” between schedule and execute
  Relatively simple (each RS remembers that it was issued)
Insns. stay in scheduler
  Ensure they are not re-scheduled
  Not too bad
    Dependents issued in order
    Mis-speculation known before Exec
Sched
PayLd
Exec
Exec
Exec
Sched
PayLd
Exec
Sched
PayLd
Exec
Sched
PayLd
Exec
Sched
PayLd
Exec
Sched
PayLd
Exec
Sched
PayLd
Exec
Sched
PayLd
Exec
?
  May squash non-dependent instructions

## Slide 29: Squashing (2/3)
Selective squashing with “load colors”
  Each load assigned a unique color
  Every dependent “inherits” parents’ colors
  On load miss, the load broadcasts its color
    Anyone in the same color group gets squashed
An instruction may end up with many colors
…
…
  Tracking colors requires huge number of comparisons

## Slide 30: Squashing (3/3)
Can list “colors” in unary (bit-vector) form
  Each insn.’s vector is bitwise OR of parents’ vectors
Load R1 = 16[R2]
1
0
0
0
0
0
0
0
Add R3 = R1 + R4
1
0
0
0
0
0
0
0
Load R5 = 12[R7]
1
0
0
0
0
0
0
0
Load R8 = 0[R1]
1
0
1
0
0
0
0
0
Load R7 = 8[R4]
1
0
0
0
0
0
0
0
Add R6 = R8 + R7
1
0
1
0
0
0
0
1
X
X
X
  Allows squashing just the dependents
Notes: Hardware can still be pretty expensive; consider a modern Core 2 with a 32-entry LDQ… you would need 32 load colors to track everything (and there are some weird corner cases where a color cannot be reallocated before all “consumers” of that color have also executed).

## Slide 31: Scheduler Allocation (1/3)
Allocate in order, deallocate in order
  Very simple!
Reduces effective scheduler size
  Insns. executed out-of-order … RS entries cannot be reused
Circular Buffer
Head
Tail
Tail
  Can be terrible if load goes to memory
Notes: This is specific to the allocation of the RS entries.

## Slide 32: Scheduler Allocation (2/3)
Arbitrary placement improves utilization
Complex allocator
  Scan availability to find N free entries
Complex write logic
  Route N insns. to arbitrary entries
RS Allocator
Entry availability
bit-vector
0
0
0
0
1
0
0
1
0
0
0
0
0
1
1
1

## Slide 33: Scheduler Allocation (3/3)
Segment the entries
  One entry per segment may be allocated per cycle
  Each allocator does 1-of-4
    Instead of 4-of-16 as before
  Write logic is simplified
Still possible inefficiencies
  Full segments block allocation
  Reduces dispatch width
0
0
1
0
1
0
1
0
0
0
0
1
0
1
1
0
Alloc
Alloc
Alloc
Alloc
A
B
C
D
X
Free RS entries exist, just
not in the correct segment
0

## Slide 34: Select Logic
Goal: minimize DFG height (execution time)
NP-Hard
  Precedence Constrained Scheduling Problem
  Even harder: entire DFG is not known at scheduling time
    Scheduling insns. may affect scheduling of not-yet-fetched insns.
Today’s designs implement heuristics
  For performance
  For ease of implementation
Notes: The Select Logic is also sometimes called a “picker”.
The NP-Hard part is even if you were given the entire DFG, you still couldn’t efficiently find the optimal schedule. The assumption that you can see the entire DFG is obviously false in a processor. This is also harder because instruction latencies are not constant (i.e., changing the schedule can change whether certain loads hit or miss).

## Slide 35: Simple Select Logic
Scheduler Entries
1
S entries
yields O(S)
gate delay
Grant0 = 1
Grant1 = !Bid0
Grant2 = !Bid0 & !Bid1
Grant3 = !Bid0 & !Bid1 & !Bid2
Grantn-1 = !Bid0 & … & !Bidn-2
1
x0
x1
x2
x3
x4
x5
x6
x7
x8
grant0
xi = Bidi
granti
grant1
grant2
grant3
grant4
grant5
grant6
grant7
grant8
grant9
O(log S) gates
Notes: This just selects the first ready instruction, where “first” is simply determined by physical location in the scheduler (top entry has highest priority). In this example, a grant may be seen by an entry that is not ready in which case the grant is simply ignored (the circuit will ensure that only one ready entry will ever receive a grant).

## Slide 36: Random Select
Insns. occupy arbitrary scheduler entries
  First ready entry may be the oldest, youngest, or in middle
  Simple static policy results in “random” schedule
    Still “correct” (no dependencies are violated)
    Likely to be far from optimal

## Slide 37: Oldest-First Select
Newly dispatched insns. have few dependencies
  No one is waiting for them yet
Insns. in scheduler are likely to have the most deps.
  Many new insns. dispatched since old insn’s rename
Selecting oldest likely satisfies more dependencies
  … finishing it sooner is likely to make more insns. ready
Notes: The older instructions also have a higher chance of blocking up resource allocation (e.g., full ROB, LDQ, etc.)

## Slide 38: Implementing Oldest First Select (1/3)
B
A
C
D
E
F
H
Write instructions
into scheduler in
program order
G
E
F
H
G
Compress Up
K
L
E
F
H
G
I
J
Newly
dispatched
I
J
B
D
Notes: Alpha 21264 used a compressing scheduler.
The fading instructions indicate those which have been selected and sent off to execution.

## Slide 39: Implementing Oldest First Select (2/3)
Compressing buffers are very complex
  Gates, wiring, area, power
Ex. 4-wide
Need up to
shift by 4
An entire
instruction’s
worth of
data: tags,
opcodes,
immediates,
readiness, etc.
Notes: Lots of multiplexing, huge amounts of wiring. Remember that any arbitrary four slots may be vacated in any given cycle.

## Slide 40: Implementing Oldest First Select (3/3)
B
C
A
D
E
F
H
G
4
6
0
5
3
1
7
2
0
3
∞
2
2
0
0
Age-Aware Select Logic
Grant
  Must broadcast grant age to instructions
Notes: Each box in the select logic is a MIN operation, and passes the lower timestamp (older instruction) onward to the right. Non-ready instruction effectively present a timestamp of ∞ to the select logic. At the root of the tree, the last timestamp is that of the oldest AND ready instruction.

## Slide 41: Problems in N-of-M Select (1/2)
B
C
A
D
E
F
H
G
4
6
0
5
3
1
7
2
Age-Aware 1-of-M
Age-Aware 1-of-M
∞
Age-Aware 1-of-M
∞
∞
N layers  O(N log M) delay
O(log M) gate delay / select
Notes: This is a serial selection… Everyone bids to the first select logic. If you’re not selected, then you continue bidding on the next select logic circuit (if you are selected, then your timestamp gets changed to ∞ to indicate that you don’t need to bid anymore). Each select logic has O(log M) gate delay assuming a tree-like implementation from the last lecture, but we have N such circuits in series.

## Slide 42: Problems in N-of-M Select (2/2)
Select logic handles functional unit constraints
  Maybe two instructions ready this cycle … but both need the divider
DIV
DIV
ADD
XOR
3
LOAD
1
4
2
5
MUL
6
BR
7
ADD
8
Assume issue width = 4
ADD is the 5th oldest ready
instruction, but it should be issued
because only one of the ready
divides can issue this cycle
Four oldest and ready instructions

## Slide 43: Partitioned Select
DIV
LOAD
XOR
MUL
DIV
ADD
BR
ADD
DL1
1-of-M ALU Select
1-of-M Mul/Div Select
1-of-M Load Select
1-of-M Store Select
Load
Store
N possible insns. issued per cycle
3
1
4
2
5
6
7
8
Add(2)
Div(1)
Load(5)
(Idle)
5 Ready Insts
Max Issue = 4
Actual issue is
only 3 insts
Notes: Only can achieve the maximum issue rate if you have the perfect mix of ready instructions (in this case, one add, one divide, one load and one store). The gate delay, however, is pretty reasonable since any instruction will bid to at most one select logic, and so the worst case delay is that of one select logic circuit, not N of them.

## Slide 44: Multiple Units of the Same Type
  Possible to have multiple popular FUs
1-of-M ALU Select
DIV
LOAD
XOR
MUL
DIV
ADD
BR
ADD
DL1
1-of-M ALU Select
1-of-M Mul/Div Select
1-of-M Load Select
1-of-M Store Select
Load
Store
3
1
4
2
5
6
7
8
ALU1
ALU2

## Slide 45: Chain Select Logics
ADD
ADD
2
8
Select Logic for ALU1
Select Logic for ALU2
2
8
∞
8
  Works, but doubles the select latency
Notes: This doesn’t scale as the number of similar functional units increases. Even doubling the select logic latency is really not desirable.

## Slide 46: Select Binding (1/2)
XOR
SUB
2
8
Select Logic for ALU1
Select Logic for ALU2
2
1
During dispatch/alloc, each
instruction is bound to one
and only one select logic
ADD
4
1
ADD
5
1
CMP
7
2

## Slide 47: Select Binding (2/2)
XOR
SUB
2
8
Select Logic for ALU1
Select Logic for ALU2
2
1
ADD
4
1
ADD
5
1
CMP
3
2
Not-Quite-Oldest-First:
Ready insns are aged 2, 3, 4
Issued insns are 2 and 4
XOR
SUB
2
8
Select Logic for ALU1
Select Logic for ALU2
2
1
ADD
4
1
ADD
5
1
CMP
3
2
(Idle)
Wasted Resources:
3 instructions are ready
Only 1 gets to issue
Notes: Bob Colwell’s chapter in Shen and Lipasti’s book indicate that they used some sort of load-balancing approach for assigninging select ports to instructions. This could probably be done by assigning an instruction to a valid port with the least number of unexecuted instructions already bound to that port. This doesn’t guarantee that the situation depicted on the right can’t happen, but it hopefully reduces the frequency.

## Slide 48: Make N Match Functional Units?
ALU1
ALU2
ALU3
M/D
Shift
FAdd
FM/D
SIMD
Load
Store
ADD
5
LOAD
3
MUL
6
  Too big and too slow
Notes: M/D = Mul/Div
This assigns one dedicated select logic circuit for each of the functional units… obviously going to cost you a lot of hardware.

## Slide 49: Execution Ports (1/2)
Divide functional units into P groups
  Called “ports”
Area only O(P2M log M), where P << F
Logic for tracking bids and grants less complex (deals with P sets)
ADD
3
LOAD
5
ADD
2
MUL
8
Port 0
Port 1
Port 2
Port 3
Port 4
ALU1
ALU2
ALU3
M/D
Shift
FAdd
FM/D
SIMD
Load
Store

## Slide 50: Execution Ports (2/2)
More wasted resources
Example
  SHL issued on Port 0
  ADD cannot issue
  3 ALUs are unused
XOR
SHL
2
1
Select Logic for Port 0
Select Logic for Port 1
1
0
ADD
4
2
ADD
5
0
CMP
3
1
ALU1
Shift
ALU2
Load
Select Logic for Port 1
ALU3
Store
Notes: Oh well, too bad!

## Slide 51: Port Binding
Assignment of functional units to execution ports
  Depends on number/type of FUs and issue width
FAdd
FM/D
ALU1
ALU2
M/D
Shift
Load
Store
8 Units, N=4
Int/FP Separation
Only Port 3 needs
to access FP RF
and support 64/80 bits
ALU1
ALU2
Load
M/D
Store
Shift
FM/D
FAdd
Even distribution of
Int/FP units, more
likely to keep all
N ports busy
ALU1
ALU2
Load
Shift
M/D
Store
FAdd
FM/D
Each port need not have
the same number of FUs;
should be bound based
on frequency of usage
Notes: The middle case is better if you have, for example, a lot of FMAC’s where you need to issue both to the FAdder and the FMul.

## Slide 52: Port Assignment
Insns. get port assignment at dispatch
For unique resources
  Assign to the only viable port
  Ex. Store must be assigned to Port 2
For non-unique resources
  Must make intelligent decision
  Ex. ADD can go to any of Ports 0, 1 or 2
Optimal assignment requires knowing the future
Possible heuristics
  random, round-robin, load-balance, dependency-based, …
ALU1
ALU2
ALU3
M/D
Shift
FAdd
FM/D
SIMD
Load
Store
Port 0
Port 1
Port 2
Port 3
Port 4
Notes: … this should be obvious that the select logic binding and the execution port binding should be one and the same.

## Slide 53: Decentralized RS (1/4)
P2
Port3
Port 1
Port 0
Select for Port 3
Select for Port 2
Select for Port 1
Select for Port 0
Area and latency depend on number of RS entries
Decentralize the RS to reduce effects:
M1 entries
M2 entries
M3 entries
Select logic blocks for RSi only have
gate delay of O(log Mi)
RS1
RS2
RS3
Notes: The select logic circuits on the left have latencies of O(log(M1+M2+m3)), where as each select logic on the right is smaller (and faster).

## Slide 54: Decentralized RS (2/4)
Natural split: INT vs. FP
Port 1
Port 3
Store
Load
ALU1
ALU2
FP-Ld
FP-St
FAdd
FM/D
L1 Data Cache
FP-only wakeup
Int-only wakeup
INT
RF
FP
RF
FP Cluster
Int Cluster
Often implies non-ROB based
physical register file:
One “unified” integer
PRF, and one “unified”
FP PRF, each managed
separately with their
own free lists
Port 0
Port 2
Notes: This picture assumes no direct INT-to-FP move instructions (or the other way around).

## Slide 55: Decentralized RS (3/4)
Fully generalized decentralized RS
Over-doing it can make RS and select smaller … but tag broadcast may get out of control
Port 0
Port 1
Port 2
Port 3
Port 4
Port 5
FAdd
FM/D
ALU1
ALU2
M/D
Store
Shift
Load
FP-Ld
FP-St
MOV F/I
  Can combine with INT/FP split idea

## Slide 56: Decentralized RS (4/4)
Each RS-cluster is smaller
  Easier to implement, less area, faster clock speed
Poor utilization leads to IPC loss
  Partitioning must match program characteristics
  Previous example:
    Integer program with no FP instructions runs on 2/3 of issue width (ports 4 and 5 are unused)
Notes: Effective window size also reduced since non-FP program will never allocate instructions to the RS entries associated with ports 4 and 5.