## Slide 1: CSE 502: Computer Architecture
Branch Prediction

## Slide 2: Toxonomy of Branches
Direction:
  Conditional vs. Unconditional
Target:
  PC-encoded
    PC-relative
    Absolute offset
  Computed (target derived from register)
  Need direction and target to find next fetch group

## Slide 3: Branch Prediction Overview
Use two hardware predictors
  Direction predictor guesses if branch is taken or not-taken
  Target predictor guesses the destination PC
Predictions are based on history
  Use previous behavior as indication of future behavior
  Use historical context to disambiguate predictions
Notes: This lecture does not discuss how to predict the direction of branches (T vs. NT)… see next lecture for that.

## Slide 4: Where Are the Branches?
To predict a branch, must find the branch
L1-I
PC
1001010101011010101001
0101001010110101001010
0101010101101010010010
0000100100111001001010
  Where is the branch in the fetch group?
Notes: Main point being that if all we have is a PC, we don’t know where any branches are (if they even exist) since we haven’t even yet fetched the instructions (let alone decoded them).

## Slide 5: Simplistic Fetch Engine
L1-I
PD
PD
PD
PD
Dir
Pred
Target
Pred
Branch’s PC
+
sizeof(inst)
Fetch PC
  Huge latency (reduces clock frequency)
Notes: PD = predecoder (only does enough decode work to determine the branches)
Mux selects the first branch in the fetch group (there may be multiple branches)

## Slide 6: Branch Identification
L1-I
Dir
Pred
Target
Pred
Branch’s PC
+
sizeof(inst)
Store 1 bit per
inst, set if inst
is a branch
partial-decode
logic removed
Predecode branches on fill from L2
  High latency (L1-I on the critical path)

## Slide 7: Line Granularity
Predict fetch group without location of branches
  With one branch in fetch group, does it matter where it is?
X
X
T
X
X
N
X
X
T
N
One predictor entry
per instruction PC
One predictor entry
per fetch group
Notes: The obvious challenge is it a fetch group contains more than one branch; in such a situation, having only one predictor entry per group (rather than per instruction) will lead to aliasing problems, potentially for both direction and target prediction. This is discussed more next slide.

## Slide 8: Predicting by Line
L1-I
br1
br2
Dir
Pred
Target
Pred
+
sizeof($-line)
Correct
Dir Pred
Correct
Target Pred
br1
br2
Cache Line address
N
N
N
--
X
Y
N
T
T
Y
T
--
T
X
This is still challenging: we may
need to choose between multiple
targets for the same cache line
  Latency determined by branch predictor
Notes: Main point being that the critical path does not go through the L1-I anymore.
The side table just illustrates the point made in the comments of the previous slide: since there are two branches in this one fetch group/cacheline, this may lead to more difficult prediction scenarios.

## Slide 9: Multiple Branch Prediction
Dir Pred
Target Pred
L1-I
N
N
N
T
addr0
addr1
addr2
addr3
Scan for
1st “T”
0 1
+
LSBs of PC
sizeof($-line)
no LSBs of PC
PC
Notes: I.e., trying to make predictions for all of the branches within the cacheline at the same time.

## Slide 10: Direction vs. Target Prediction
Direction: 0 or 1
Target: 32- or 64-bit value
Turns out targets are generally easier to predict
  Don’t need to predict Not-taken target
  Taken target doesn’t usually change
Only need to predict taken-branch targets
Prediction is really just a “cache”
  Branch Target Buffer (BTB)
Target
Pred
+
sizeof(inst)
PC
Notes: Be careful about whether you add “sizeof(inst)” or “sizeof(cacheline)” to the PC (and really it’s the PC of the start of the cacheline if you’re adding “sizeof(cacheline)”).

## Slide 11: Branch Target Buffer (BTB)
V
BIA
BTA
Branch PC
Branch Target
Address
=
Valid Bit
Hit?
Branch Instruction
Address (Tag)
Next Fetch PC

## Slide 12: Set-Associative BTB
V
tag
target
Branch PC
=
V
tag
target
V
tag
target
=
=
Next PC

## Slide 13: Making BTBs Cheaper
Branch prediction is permitted to be wrong
  Processor must have ways to detect mispredictions
  Correctness of execution is always preserved
  Performance may be affected
  Can tune BTB accuracy based on cost

## Slide 14: BTB w/Partial Tags
00000000cfff9810
00000000cfff9824
00000000cfff984c
v
00000000cfff981
00000000cfff9704
v
00000000cfff982
00000000cfff9830
v
00000000cfff984
00000000cfff9900
00000000cfff9810
00000000cfff9824
00000000cfff984c
v
f981
00000000cfff9704
v
f982
00000000cfff9830
v
f984
00000000cfff9900
00001111beef9810
  Fewer bits to compare, but prediction may alias
Notes: May lead to false hits, as shown by the red address.

## Slide 15: BTB w/PC-offset Encoding
00000000cfff984c
v
f981
00000000cfff9704
v
f982
00000000cfff9830
v
f984
00000000cfff9900
00000000cfff984c
v
f981
ff9704
v
f982
ff9830
v
f984
ff9900
00000000cf ff9900
  If target too far or PC rolls over, will mispredict
Notes: Branch targets are usually close by, which results in the upper bits of the target’s address usually being identical to those in the original PC.

## Slide 16: BTB Miss?
Dir-Pred says “taken”
Target-Pred (BTB) misses
  Could default to fall-through PC (as if Dir-Pred said N-t)
    But we know that’s likely to be wrong!
Stall fetch until target known … when’s that?
  PC-relative: after decode, we can compute target
  Indirect: must wait until register read/exec

## Slide 17: Subroutine Calls
A: 0xFC34: CALL printf
B: 0xFD08: CALL printf
C: 0xFFB0: CALL printf
P: 0x1000: (start of printf)
0x1000
FC3
1
0x1000
FD0
1
0x1000
FFB
1
  BTB can easily predict target of calls
Notes: Just showing that a regular BTB handles subroutine calls without a problem. Each call site just ends up allocating a separate BTB entry, even though each entry contains the same target.

## Slide 18: Subroutine Returns
P: 0x1000: ST $RA  [$sp]
0x1B98: LD $tmp  [$sp]
A: 0xFC34: CALL printf
B: 0xFD08: CALL printf
A’:0xFC38: CMP $ret, 0
B’:0xFD0C: CMP $ret, 0
0x1B9C: RETN $tmp
0xFC38
1B9
0
1
X
  BTB can’t predict return for multiple call sites
Notes: Demonstrating the a regular BTB cannot handle accurate return address prediction when the function is called from multiple sites.

## Slide 19: Return Address Stack (RAS)
Keep track of call stack
A: 0xFC34: CALL printf
FC38
D004
P: 0x1000: ST $RA  [$sp]
…
0x1B9C: RETN $tmp
FC38
BTB
A’:0xFC38: CMP $ret, 0
FC38

## Slide 20: Return Address Stack Overflow
Wrap-around and overwrite
  Will lead to eventual misprediction after four pops
Do not modify RAS
  Will lead to misprediction on next pop
FC90
top of stack
64AC: CALL printf
64B0
???
421C
48C8
7300
Notes: Just discussing what to do when the function call depth is greater than the size of your RAS. Option 1 is probably the best. Another interesting example to consider is a simple recursive function: f() calls f(), but with a very deep level of nesting; if the recursion always happens from the same spot in the function f(), then the return addresses will always be the same, and so even though the RAS may overflow, it keeps getting overwritten with the same return address.

## Slide 21: Branches Have Locality
If a branch was previously taken…
  There’s a good chance it’ll be taken again
for(i=0; i < 100000; i++)
{
/* do stuff */
}
This branch will be taken
99,999 times in a row.

## Slide 22: Simple Direction Predictor
Always predict N-t
  No fetch bubbles (always just fetch the next line)
  Does horribly on loops
Always predict T
  Does pretty well on loops
  What if you have if statements?
  p = calloc(num,sizeof(*p));
  if(p == NULL)
  error_handler( );
This branch is practically
never taken
Notes: Assuming this is implemented in assembly as a conditional jump with error_handler as the taken target.

## Slide 23: Last Outcome Predictor
Do what you did last time
0xDC08: for(i=0; i < 100000; i++)
{
0xDC44: if( ( i % 100) == 0 )
        tick( );
0xDC50: if( (i & 1) == 1)
odd( );
}
T
N
Notes: I.e., 1-bit counter

## Slide 24: Misprediction Rates?
0xDC08:TTTTTTTTTTT ... TTTTTTTTTTNTTTTTTTTT …
100,000 iterations
How often is branch outcome != previous outcome?
2 / 100,000
TN
NT
0xDC44:TTTTT ... TNTTTTT ... TNTTTTT ...
2 / 100
0xDC50:TNTNTNTNTNTNTNTNTNTNTNTNTNTNT …
2 / 2
99.998%
Prediction
Rate
98.0%
0.0%
Notes: DC08, DC44 and DC50 refer to the hexadecimal PC’s used on the previous slide.

## Slide 25: Saturating Two-Bit Counter
0
1
FSM for Last-Outcome
Prediction
0
1
2
3
FSM for 2bC
(2-bit Counter)
Predict N-t
Predict T
Transition on T outcome
Transition on N-t outcome

## Slide 26: Example
2
T

3
T
3
T


…
3
N

N
1

T
0

0
T
1
T
T
T
T
…
T
1
1
1
1






T
1

T
…
1

0
T
1
T
2
T
3
T
3
T
…
3
T






Initial Training/Warm-up
1bC:
2bC:
Only 1 Mispredict per N branches now!
DC08: 99.999% DC44: 99.0%
  2x reduction in misprediction rate

## Slide 27: Typical Organization of 2bC Predictor
PC
hash
32 or 64 bits
log2 n bits
n entries/counters
Prediction
FSM
Update
Logic
table update
Actual outcome

## Slide 28: Typical Branch Predictor Hash
Take the log2n least significant bits of PC
May need to ignore some bits
  In RISC, insns. are typically 4 bytes wide
    Low-order bits zero
  In CISC (ex. x86), insns. can start anywhere
    Probably don’t want to shift

## Slide 29: Dealing with Toggling Branches
Branch at 0xDC50 changes on every iteration
  1bc and 2bc don’t do too well (50% at best)
  But it’s still obviously predictable
Why?
  It has a repeating pattern: (NT)*
  How about other patterns? (TTNTN)*
Use branch correlation
  Branch outcome is often related to previous outcome(s)

## Slide 30: Track the History of Branches (1/2)
PC
Previous Outcome
1
Counter if prev=0
Counter if prev=1

## Slide 31: Track the History of Branches (2/2)
PC
Previous Outcome
1
Counter if prev=0
3
0
Counter if prev=1
1
3
3
prev = 1
3
0
prediction = N
prev = 0
3
0
prediction = T
prev = 1
3
0
prediction = N
prev = 0
3
0
prediction = T
prev = 1
3
prediction = T
3
prev = 1
3
prediction = T
3
prev = 1
3
prediction = T
2

prev = 0
3
prediction = T
2
Notes: In the animated example, the left circle corresponds to the 2bC used when the previous outcome was 0, and the right corresponds to 1. The not-used counter is shaded darker.

## Slide 32: Deeper History Covers More Patterns
Counters learn “pattern” of prediction
PC
0
3
1
0
1
3
1
0
0
2
2
Previous 3 Outcomes
Counter if prev=000
Counter if prev=001
Counter if prev=010
Counter if prev=111
001  1; 011  0; 110  0; 100  1
00110011001… (0011)*

## Slide 33: Predictor Organizations
PC Hash
Different pattern for
each branch PC
PC Hash
Shared set of
patterns
PC Hash
Mix of both
Notes: Each trades off aliasing in different places. The first suffers from different static branches mapping into the same local history and counters. The second allows different static branches that exhibit the same local history to map into the same counters. The figures do not imply that the total number of branch history registers in the three figures are necessarily the same.

## Slide 34: Branch Predictor Example (1/2)
1024 counters (210)
  32 sets ( )
    5-bit PC hash chooses a set
  Each set has 32 counters
    32 x 32 = 1024
    History length of 5 (log232 = 5)
Branch collisions
  1000’s of branches collapsed into only 32 sets
PC Hash
5
5

## Slide 35: Branch Predictor Example (2/2)
1024 counters (210)
  128 sets ( )
    7-bit PC hash chooses a set
  Each set has 8 counters
    128 x 8 = 1024
    History length of 3 (log28 = 3)
Limited Patterns/Correlation
  Can now only handle history length of three
PC Hash
7
3

## Slide 36: Two-Level Predictor Organization
Branch History Table (BHT)
  2a entries
  h-bit history per entry
Pattern History Table (PHT)
  2b sets
  2h counters per set
Total Size in bits
  h2a + 2(b+h)2
PC Hash
a
b
h
Each entry is a 2-bit counter

## Slide 37: Classes of Two-Level Predictors
h = 0 or a = 0 (Degenerate Case)
  Regular table of 2bC’s (b = log2counters)
h > 0, a > 0
  “Local History” 2-level predictor
  Predict branch from its own previous outcomes
h > 0, a = 0
  “Global History” 2-level predictor
  Predict branch from previous outcomes of all branches

## Slide 38: Why Global Correlations Exist
Example: related branch conditions
  p = findNode(foo);
  if ( p is parent )
  do something;
  do other stuff; /* may contain more branches */
  if ( p is a child )
  do something else;
Outcome of second
branch is always
opposite of the first
branch
A:
B:

## Slide 39: A Global-History Predictor
PC Hash
b
h
Single global
Branch History Register (BHR)
PC Hash
b
h
{b,h}

## Slide 40: Tradeoff Between B and H
For fixed number of counters
  Larger h  Smaller b
    Larger h  longer history
      Able to capture more patterns
      Longer warm-up/training time
    Smaller b  more branches map to same set of counters
      More interference
  Larger b  Smaller h
    Just the opposite…

## Slide 41: Combined Indexing (1/2)
“gshare” (S. McFarling)
PC Hash
k
XOR
k = log2counters
k

## Slide 42: Combined Indexing (2/2)
Not all 2h “states” are used
  (TTNN)* uses ¼ of the states for a history length of 4
  (TN)* uses two states regardless of history length
Not all bits of the PC are uniformly distributed
Not all bits of the history are uniformly correlated
  More recent history more likely to be strongly correlated
PC Hash
k
XOR
k = log2counters
k

## Slide 43: Combining Predictors
Some branches exhibit local history correlations
  ex. loop branches
Some branches exhibit global history correlations
  “spaghetti logic”, ex. if-elsif-elsif-elsif-else branches
Global and local correlation often exclusive
  Global history hurts locally-correlated branches
  Local history hurts globally-correlated branches

## Slide 44: Tournament Hybrid Predictors
Pred0 | Pred1 | Meta Update
 |  | ---
 |  | Inc
 |  | Dec
 |  | ---
Pred0
Pred1
Meta-
Predictor
Final Prediction
table of 2-/3-bit counters
If meta-counter MSB = 0,
use pred0 else use pred1

## Slide 45: Pros and Cons of Long Branch Histories
Long global history provides context
  More potential sources of correlation
Long history incurs costs
  PHT cost increases exponentially: O(2h) counters
  Training time increases, possibly decreasing accuracy

## Slide 46: Predictor Training Time
Ex.: prediction equals opposite for 2nd most recent
Hist Len = 2
4 states to train:
  NN  T
  NT  T
  TN  N
  TT  N
Hist Len = 3
8 states to train:
  NNN  T
  NNT  T
  NTN  N
  NTT  N
  TNN  T
  TNT  T
  TTN  N
  TTT  N

## Slide 47: Branch Predictions Can Be Wrong
How/when do we detect a misprediction?
What do we do about it?
  Re-steer fetch to correct address
  Hunt down and squash instructions from the wrong path

## Slide 48: Branch Mispredictions in the Pipeline (1/2)
Fetch
(IF)
Decode
(ID)
Dispatch
(DP)
Execute
(EX)
T
br
A
B
D
br
br
br
…
A
A
A
Mispred Detected
B
B
D
Multiple speculatively fetched
basic blocks may be in flight
at the same time!
4-wide superscalar

## Slide 49: Branch Mispredictions in the Pipeline (2/2)
IF
ID
DP
EX
Direction prediction, target prediction
We know if branch is return, indirect jump, or phantom branch
RAS
iBTB
If indirect target, can potentially read target from RF
Squash instructions in BP, L1-I, and ID
Re-steer BP to target from RF
Detect wrong direction or wrong target (indirect)
Squash instructions in BP, L1-I, ID and DP, plus rest of pipeline
Re-steer BP to correct next PC
Squash instructions in BP and L1-I-lookup
Re-steer BP to new target from RAS/iBTB
Notes: iBTB = indirect branch target buffer (just another BTB, but perhaps indexed with some additional information, e.g., branch history, instead of only the PC).
Whether or not you can detect an indirect target misprediction at the time of register read depends on datapath assumptions. To do so, you would have to directly route the predicted target to somewhere near the RF, add a comparator there, and then route out the appropriate signals back to the front-end. It’s probably easier to just unify it all at execution so that direction and target mispredictions share/use the same misprediction recovery logic.

## Slide 50: Phantom Branches
May occur when performing multiple bpreds
PC
BPred
T
4 preds corresponding to
4 possible branches in
the fetch group
L1-I
BR
XOR
BR
ADD
A
B
C
D
X
Z
Fetch: ABCX… (C appears to be a branch)
After fetch, we discover C cannot be taken because it is not
even a branch! This is a phantom branch.
Should have fetched: ABCDZ…
T
N
N
Notes: With multiple branch prediction and no pre-decoding, it’s possible (due to aliasing in the predictor(s), partial tags, etc.) that you predict a taken branch when a branch does not even exist in the current fetch group.

## Slide 51: Front-End Hardware Organization
L1-I
BPred
BTB
+
sizeof(L1-I-line)
ID
RAS
iBTB
uncond br
!=
actual target
push on call
pop
on
retn
no branch
is retn
is indir
control
NPC
PC
EX
Notes: Note that the Zesto simulator has all prediction structures in the fetch stage (RAS and iBTB are used in parallel with the bpred and regular BTB… similar to if you assumed the presence of some sort of decode prediction). We’re not entirely sure where each predictor is located in real pipelines, but it’s not too hard to think about what is necessary to make each possibility work.

## Slide 52: Speculative Branch Update (1/3)
Ideal branch predictor operation
  Given PC, predict branch outcome
  Given actual outcome, update/train predictor
  Repeat
Actual branch predictor operation
  Streams of predictions and updates proceed parallel
A
Predict:
B
C
D
E
F
G
Update:
A
B
C
D
E
F
G
time
  Can’t wait for update before making new prediction

## Slide 53: Speculative Branch Update (2/3)
BHR update cannot be delayed until commit
  But outcome not known until commit
A
Predict:
B
C
D
E
F
G
Update:
A
B
C
D
E
F
G
011010
011010
011010
011010
011010
110101
BHR:
Branches B-E all predicted with
the same stale BHR value
Notes: Branch F would also likely use a stale BHR value unless the update from A happens at the very start of the cycle.

## Slide 54: Speculative Branch Update (3/3)
Update branch history using predictions
  Speculative update
If predictions are correct, then BHR is correct
What happens on a misprediction?
  Commit-time BHR recovery
  Execution-time BHR recovery

## Slide 55: Commit-time BHR recovery
BPred
Lookup
0110100100100…
Speculative BHR
BPred
Update
Actual BHR
Mispredict!
Notes: Recovery during commit/retirement of the mispredicted branch.

## Slide 56: Execution-time BHR recovery
Commit-time may delay misprediction recovery
Instead, “checkpoint” BHR at time of prediction
  Roll back to checkpoint for recovery
  Must track where to roll back to
  In-flight branches limited by number of checkpoints
Load
Br
Cache miss to DRAM
Executed, but
can’t recover
until load is done
Notes: The figure is just showing an example where waiting until commit to recover can cost you a lot of time.

## Slide 57: Overriding Branch Predictors (1/2)
Use two branch predictors
  1st one has single-cycle latency (fast, medium accuracy)
  2nd one has multi-cycle latency, but more accurate
  Second predictor can override the 1st prediction
  Get speed without full penalty of low accuracy

## Slide 58: Overriding Branch Predictors (2/2)
Predict
A’
Fast 1st Pred
2-cycle
Pipelined L1-I
Slower 2nd Pred
A
Predict
B
Predict
A’
Predict
B’
Fetch A
B
Predict
C
Predict
B’
Predict
A’
Predict
C’
Fetch B
Fetch A
If A=A’ (both preds
agree), done
If A != A’, flush A, B andC
restart fetch with A’
Z
Predict
A