## Slide 1: CSE 506: Operating Systems
Disk Scheduling

## Slide 2: Key to Disk Performance
Don’t access the disk
  Whenever possible
Cache contents in memory
  Most accesses hit in the block cache
Prefetch blocks into block cache (a.k.a. read-ahead)
  When OS accesses disk, get next few blocks too
    Keep them in block cache
  If access hits on prefetched block
    Read the next few blocks in the background
  Avoids demand access to the disk

## Slide 3: Caching + Throughput
Most reads and writes to disk are asynchronous
  Dirty data can be buffered and written at OS’s leisure
  Most reads hit in block cache – read-ahead works
How to optimally order pending disk I/O requests?
  Hint: it isn’t first-come, first-served

## Slide 4: Another view of disk accesses
Between block cache and disk, there is a queue
  All disk requests wait in this queue
  Requests are a tuple of (block #, read/write, buffer addr)
Requests can be reordered
  To achieve best performance across all requests
What reordering heuristic to use? If any?
  Heuristic is called the IO Scheduler

## Slide 5: A simple disk model
Disks are slow
  Moving parts much slower than circuits
  Flash storage is faster
    Still multiple orders of magnitude slower than memory
Programming interface: simple array of sectors (blocks)
Physical disk layout:
  Concentric “cylinders” of blocks on a platter
    Two tracks, one on each side
  Ex.: sectors 0-9 on innermost track, 10-19 on next track, etc.
  Disk arm (with heads attached) moves between tracks
  Platter rotates under disk head to align w/ requested sector

## Slide 6: Disk Model
0
1
2
3
4
5
6
7
Each block on a sector
Disk
Arm
Disk Head reads at granularity of entire sector
Disk spins at a constant speed.
Tracks rotate underneath head.

## Slide 7: Disk Model
Disk
Arm
Concentric tracks
8
9
10
11
12
13
17
18
19
20
21
0
1
2
3
4
5
6
7
14
15
16
22
23
Gap between 7 and 8 accounts for seek time
Disk head seeks to different tracks

## Slide 8: Many Tracks
Disk
Arm

## Slide 9: Several (~4) Platters
Platters spin together at same speed
Each platter has two heads; All heads seek together on arm

## Slide 10: 3 key latencies
I/O delay: Time to read/write a sector
Rotational delay: Time for track to rotate under head
  Note: disk rotates continuously at constant speed
Seek delay: Time to move disk arm to cylinder

## Slide 11: Greedy IO Scheduler
Op. latency is function of arm and cylinder position
Each request changes these values
Idea: build a model of the disk
  Use delay values from measurement or manuals
  Use math to evaluate latency of each pending request
  Greedy algorithm: always select lowest latency

## Slide 12: Problem with Greedy?
“Far” requests will starve
Disk head may just hover around the “middle” tracks

## Slide 13: Elevator Algorithms (SCAN)
Arm moves in continuous “sweeps” in and out
  Reorder requests within a sweep
    Closest block in direction of travel is next to be read
    Request that was just passed has to wait for sweep to return
Prevents starvation
  Sectors “inside” or “outside” serviced after bounded time
Reasonably good throughput
  Sort requests to minimize seek latency
Simple to code
  Programming model hides low-level details

## Slide 14: Elevator Algorithms (C-SCAN)
SCAN is not fair
  Cylinders in the middle get serviced ~twice as often
    Likely to be handled when arm travels in either direction
Only perform ops when moving in one direction
  Once the end is reached, quickly go to the beginning
More fair
  But probably lower average performance

## Slide 15: Pluggable Schedulers
Linux allows the disk scheduler to be replaced
  Just like the CPU scheduler
Can choose a different heuristic that favors:
  Fairness
  Real-time constraints
  Performance

## Slide 16: Complete Fairness Queue (CFQ)
Idea: Add a second layer of queues (one per process)
  Round-robin promote them to the “real” queue
Goal: Fairly distribute disk bandwidth among tasks
Problems?
  Overall throughput likely reduced
  Ping-pong disk head around

## Slide 17: Deadline Scheduler
Associate expiration times with requests
Prioritize requests closer to expiration
  Constrains reordering to ensure forward progress
Good for real-time applications

## Slide 18: Anticipatory Scheduler
Idea: Try to anticipate locality of requests
If process P issues bursts of requests for close blocks
  If a request from P arrives
    Hold request in queue for a while
    Hope that more “nearby” requests come in
  Eventually, schedule all pending requests at once
    Coalesce adjacent requests

## Slide 19: Optimizations at Cross-purposes
The disk itself does some optimizations
  Caching
    Disks have their own caches
    And do their own read-ahead
  Reordering requests internally
    Disk protocols (e.g., SAS) allow many outstanding commands
      Can’t assume that requests are serviced in order
  Bad sectors can be remapped to “spares”
    Problem: disk arm flailing on an old disk